HAAKE RheoWin Version 4.63.0004

Contents of this document

1 Downloading and installing

1.1 Download the RheoWin files

1.2 Installation of RheoWin 4

1.2.1 Installation

1.2.2 RheoWin and Windows Users (Administrators, PowerUsers, Users, etc.)

1.3 RheoWin 4 license key

2 What's new

2.1 Version 4.00.0000

2.2 Version 4.00.0001

2.3 Version 4.00.0002

2.4 Version 4.00.0003

2.5 Version 4.00.0004

2.6 Version 4.00.0005

2.7 Version 4.00.0006

2.8 Version 4.00.0007

2.9 Version 4.10.0000

2.10 Version 4.10.0001

2.11 Version 4.10.0002

2.12 Version 4.10.0003

2.13 Version 4.10.0004

2.14 Version 4.10.0005

2.15 Version 4.10.0006

2.16 Version 4.10.0007

2.17 Version 4.20.0000

2.18 Version 4.20.0001

2.19 Version 4.20.0002

2.20 Version 4.20.0003

2.21 Version 4.20.0004

2.22 Version 4.20.0005

2.23 Version 4.30.0000

2.24 Version 4.30.0001

2.25 Version 4.30.0002

2.26 Version 4.30.0004

2.27 Version 4.30.0005

2.28 Version 4.30.0007

2.29 Version 4.30.0008

2.30 Version 4.30.0009

2.31 Version 4.30.0010

2.32 Version 4.30.0011

2.33 Version 4.30.0012

2.34 Version 4.30.0013

2.35 Version 4.30.0014

2.36 Version 4.30.0015

2.37 Version 4.30.0016

2.38 Version 4.30.0020

2.39 Version 4.30.0021

2.40 Version 4.30.0022

2.41 Version 4.30.0023

2.42 Version 4.30.0024

2.43 Version 4.30.0025

2.44 Version 4.40.0003

2.45 Version 4.41.0000

2.46 Version 4.41.0006

2.47 Version 4.41.0019

2.48 Version 4.50.0003

2.49 Version 4.50.0010

2.50 Version 4.50.0011

2.51 Version 4.50.0012

2.52 Version 4.50.0013

2.53 Version 4.50.0017

2.54 Version 4.60.0000

2.55 Version 4.60.0001

2.56 Version 4.61.0000

2.57 Version 4.61.0003

2.58 Version 4.62.0000

2.59 Version 4.62.0003

2.60 Version 4.63.0000

2.61 Version 4.63.0001

2.62 Version 4.63.0002

2.63 Version 4.63.0003

2.64 Version 4.63.0004

3 Limitations and known problems

4 Contact Thermo Fisher Scientific

============================================================

1 Downloading and installing

This is a fully executable version of RheoWin. Please note that in order to be able to

install RheoWin on your computer you need a RheoWin 4 License Key.

RheoWin 4 currently supports the following HAAKE rheometers and viscometers: MARS 60, MARS 40, MARS III, MARS II, MARS I, RheoStress 6000, RheoStress 3000, RheoStress 600, 
RheoStress 300, RheoStress 150, RheoStress 80, RheoStress 75, Rotovisco 20, Viscotester iQ, Viscotester iQ Air, Viscotester 550, Viscotester D, Viscotester E, VT6L, VT6R, VT7L, VT7R, VT7L-plus, VT7R-plus, RotoVisco 1, RheoStress 1 and RheoScope 1.

RheoWin 4 does not support older instruments like the RS100, RS50, RT10, VT500, 
VT501 and the RV20+RC20/RV30 with CV20, CV100, M5 or M10.

RheoWin 4.63.00xx has been tested to run under the following Windows operating systems:

- Windows XP 32-bit

- Windows 7 32-bit and 64-bit

- Windows 8 32-bit and 64-bit

- Windows 8.1 32-bit and 64-bit

- Windows 10 32-bit and 64-bit

RheoWin 4.63.00xx has not been tested and is consequently not supported for use under Windows Vista! It is strongly recommend to use Windows 7 or newer instead.

RheoWin 4.63.00xx will NOT run and/or is not supported under Windows 3.x, Windows NT3.x, Windows 95, Windows 98, Windows 98 SE, Windows ME, Windows NT 4.0 and Windows 2000.

1.1 Download the RheoWin files

Download the following *.ZIP file and copy it to a (temporary) directory on your 
hard drive.

Files : Rhw46300xx_complete.zip

Then unzip the *.ZIP file using any suitable unzip program. In case you do not

have an (UN)ZIP program you can download a freeware ZIP program called FreeZip from the

following Web-site : "http://www.ozemail.com.au/~nulifetv/freezip" .

1.2 Installation of RheoWin 4

RheoWin 4 can be installed parallel to an existing RheoWin 3.xx and/or RheoWin 2.xx installation if needed. Please note that RheoWin 4 can read RheoWin 2.xx and 3.xx data, job and page files (backward compatibility), but that RheoWin 2.xx can NOT read RheoWin 3.xx and 4.xx files, also RheoWin 3.xx and can NOT read RheoWin 4.xx files!

RheoWin 2.xx, 3.xx and 4.xx should ALWAYS be installed in different directories.

RheoWin 4.63.00xx can be installed, as an Upgrade installation, over an existing RheoWin 4.20.00xx, RheoWin 4.30.00xx or RheoWin 4.4x.00xx version, without deinstalling the older version first. In this case the settings from the previous installation are automatically used for the new version.

1.2.1 Installation

Here's how to install RheoWin:

1) Please read the document new.doc BEFORE installing RheoWin 4!

2) Please note that (Windows) Administrator rights are needed to install RheoWin!

3a) Upgrade installation:

In case the settings of the previous installation should be used used for the new 
    installation the previous version must not be deinstalled before the new version is 
    installed. 
    Please note: The 'upgrade installation' can only be used for an existing 
    RheoWin 4.20.00xx, RheoWin 4.30.00xx or RheoWin 4.4x.00xx installation! 
    Please note: For older RheoWin versions (version 4.10.00xx and older) the 'Upgrade 
    installation' method can not be used, that means that the 'New installation' method
    (see 3b below) must be used, in this case the settings of the previous installation
    will not be available in the new installation.

3b) New installation:

Deinstall (remove) any previous RheoWin 4 version first (if applicable):

Click the Windows Start button, then select Settings, then select Control Panel, 
    in the Control Panel select Add or Remove Programs, in the list of programs select 
    HAAKE RheoWin and then click on the Change/Remove button and follow the instructions.
    
    Please note: In this case the settings from a previous installation will be lost and can 
    not be automatically used for the subsequent new installation!

4a) Starting the installation program from a directory on your harddisk in 
    which you unzipped the *.ZIP file :

To install RheoWin from harddisk go to the (temporary) directory in which

you unzipped the *.ZIP file after downloading. Please make sure that you

have the following file in that directory:  Setup.exe

To start the installation please run the Setup.exe program.

4b) Starting the installation program from  the RheoWin CD :
    This CD is "self-starting", just click on "Install HAAKE RheoWin 4" to start the installation.

In case the installation screen does not come up automatically you can start it by

double-clicking on the file "index.htm" in the Windows explorer, this will show the 
    installation screen in your web-browser.

You can also start the installation by run the setup.exe program from the RheoWin

directory on the CD

The installation program will guide you through the installation. Please make sure that you

have a RheoWin 4 License Key (see below) readily available since the installation program

will ask for this.

1.2.2 RheoWin and Windows Users (Administrators, PowerUsers, Users, etc.)

Windows users with the default Administrator or PowerUser rights will be able to run RheoWin without the need for any modifications to Windows settings.

For Windows users with the default Users rights an Administrator has to make sure that those users have read access to the RheoWin 4 main directory (by default c:Program Files\Thermo\RheoWin) and all its subdirectories, as well as read and write (!) access to the

HKEY_USERS\.DEFAULT\Software\Thermo\RheoWin 
key in the windows registry and the following two directories and all their subdirectories

C:\Documents and Settings\All Users\Application Data\Thermo\RheoWin

C:\Documents and Settings\All Users\Documents\Thermo\RheoWin.

The names of these directories are dependent of the operating system (Windows XP, Vista etc.) and the language of the operating system, see chapter 2.1 below.

Microsoft advices programmers to save application and user data in the above mentioned directories by default, but strange enough does not give Windows users with the default Users rights write access to these directories!

1.3 RheoWin 4 Licence Key

In order to be able to install this version of RheoWin on your computer you will need a 
RheoWin 4 License Key. A Key-Diskette from a previous version of RheoWin (version 2.x) or a RheoWin 3 License Key will NOT enable you to install RheoWin 4.

The keys for RheoWin 4 consist of a company name, serial number and the key code. When you receive the key per e-mail this information will be stored in a *.txt file which can 
be opened and viewed by using any text-editor (Notepad, Write, Word, etc.)

The key information must either be entered manually (as in previous versions) or loaded from the supplied *.txt file (this is new starting from version 4.40) during the installation process.

In order to be able to install the new tools for FDA 21 CFR part 11 compliance, a separate second License Key is needed. Separate keys are also needed to install the TTS (Time Temperature Superposition) tool, the Spectra calculation tool, the MWD tool as well as some other optional software features.

License Keys for RheoWin 4 are available on request only !

----------

2 What's new

2.1 Version 4.00.0000

(Released 15.07.2008)

Below is a list of things that are new and/or changed in version 4.00.0000 compared with 
version 3.61.0004 of RheoWin. This list is not complete yet!!

Below is a list of things that are new and/or changed in version 4.00.0000 compared with version 3.61.0004 of RheoWin.

- Installation

- New Keys

- In order to be able to install this version of RheoWin on your computer you will need a 
      New RheoWin 4 License Key. 
      A Key-Diskette for RheoWin 2.xx or a RheoWin 3 License Key will NOT enable you 
      to install RheoWin 4.

- General

- RheoWin 4.x can be installed and used parallel to RheoWin 3.x on one computer but 
      not at the same time!

- In order to comply with the far more stringent requirements of Windows Vista (relativ to
      Windows XP) regarding the storage of data and the use of certain parts of the Windows
      registry, RheoWin 4.x uses different paths for the program files and for data, job, 
      template, page, report, etc. files than RheoWin 3. It also uses a different registry key.

The program file path, the program data file path, the user data file path and the registry 
      path of RheoWin 4 comply with the Microsoft recommendations for Windows XP and
      Windows Vista.

- Path for program *.exe, *.dll, etc. files
    - The RheoWin program is now installed in the

C:\Program Files\Thermo\RheoWin 
      directory and the subdirectories of that directory,

- Path for program data files
    - The RheoWin program data files are now installed in the

Windows XP (language dependend)

C:\Documents and Settings\All Users\Application Data\Thermo\RheoWin

C:\Dokumente und Einstellungen\All Users\Anwendungsdaten\Thermo\RheoWin

Windows VISTA and Windows 7

C:\ProgramData\Thermo\RheoWin

directory and the subdirectories of that directory. 
      Program data files are files that are automatically created and modifies by the program
      without direct user interaction. Under normal circumstances a user does not need to 
      access to these files. Below is a list with which files are stored where.
      In the main RheoWin directory:

Rheowin.log    (the main RheoWin log file, used for debugging only)
      In the RheoWin\Elmdll directory:

elmdll.ini         (ini file for the RheoWin elements, used for special options only)

In the RheoWin\Drivers directory:

drivers.flp        (file in which all DeviceManager settings are stored)

drivers.ini        (ini file for the Rheometer drives, used for special options only)

*. log              (communication log files, used for debugging only)
           *.err                (communication error files, used for debugging only)
           *.msc             (exported MSC table)
           *.mtc              (exported MTC table)

In the RheoWin\Autosave directory:

autosave.rwd   (autosave copy of the last job data file)

Drivers_Autosave_x.xx.xx.flp (autosave copy of the last drivers.flp file)

Drivers_Setup_x.xx.xx.flp (autosave copy of the installation drivers.flp file)

In the RheoWin\UMS directory:

UMS.mdb       (the UserManagement settings database file)

Please note: In order to be able the see the directory mentioned above in the 
                           Windows Explorer, the option Show hidden files and folder on the 
                           View page of the Folder Options dialog in Window Explorer must 
                           be active. To open this dialog click on Tools in the Windows
                           Explorers main menu and then select the Folder Options command.

- Path for user data files

- Path for user data files

- The RheoWin user data files are now installed in the

Windows XP  (language dependend)

C:\Documents and Settings\All Users\Shared Documents\Thermo\RheoWin

C:\Dokumente und Einstellungen\All Users\Gemeinsame Dokumente\Thermo\RheoWin

Windows VISTA and Windows 7  (language dependend)

C:\Users\Public\Public Documents\Thermo\RheoWin

C:\Benutzer\Öffentlich\Öffentliche Dokumente\Thermo\RheoWin

directory and the subdirectories of that directory. 
      User data files are files that are directly created and modified by the user. 
      Below is a list with which files are stored where.
      In the RheoWin\Data directory:

*.rwd     (data files)

In the RheoWin\Job directory:

*.rwj      (job files)

In the RheoWin\Page directory:

*.rwp     (page files)

In the RheoWin\Report directory:

*.lst      (report template files)

In the RheoWin\Template directory:

*.gds     (graph template files)

*.tds      (table template files)

*.rwt      (job template files)

*.rwl      (page layout template files)

- Registry path

- In the Windows registry RheoWin now uses the following main key entry:

HKEY_USERS\.DEFAULT\Software\Thermo\RheoWin

- Font installation

- The font installation has been modified. The messagebox anouncing the font instalation

at the end of the installation has been removed.

- Supported rheometers

- Drivers for the RheoStress RS100, 1 Ncm version and 5 Ncm version, as well as the
      RS50 are not part of the installation anymore. 
      For these instruments RheoWin 3.61 or earlier should be used.

- UserManager

- There are new per User(group) definable privileges for the Elements/Job/Template explorer
    (in JobManager) and the Data/Page/Template explorer (in DataManager) for:
     • Opening files.

• Moving files and directories and renaming directories.

• Deleting files and directories.
     • Changing the root directory of an explorer tree.

- Rheometer and auxillary drivers

- Drivers for MARS

- There is no lower limit for the accepted value for the set rotational speed anymore. 
      The lowest rpm values achieved with the new CR-control loop and certain samples are
      in the range of 10^-7 to 10^-9 rpm.

- Drivers for MARS and Simulator --> Acquiring images

- RheoWin can now acquire and save color images from a suitable camera.
      Please note: We have tested this with certain USB-Webcams only. Currently we 
                           can not guarantee that this will work with other cameras!

- RheoWin is now compatible with the Foculus 323TB camera from the company 
      NET GmbH. This camera is now shipped with the RheoScope module.
      With this camera exposure times down to 1µs are possible. When using an image 
      size of 512x384 pixels or smaller, a frame rate of up to 58 fps is possible without 
      losing on image quality.

- The method used to save data and images in files was modified. Previously the 
      maximum file size was 4 GB, now the maximum file size 4.295e+09GB (theoretically...)
  - Driver for pressure sensor

- The driver now not only the supports the older GMH 3110 but also the new GMH 3111
      pressure sensor from Greisinger.

- DeviceManager

- Temperature offset tables

- Temperature offset tables can now be exported and imported. The tables can not be 
      read from the instruments yet!!!
  - Editor for Drivers.ini

- By clicking with the right mouse key on one of the three icons on the left side of the 
      DeviceManager dialog the user can launch an editor for modifying the Drivers.ini file. 
      Please note: Do not change any setting in the drivers.ini file unless you know 
                           what you are doing!

- General

- New XML data format

- RheoWin can now save and load data in an XML file format defined by an IUPAC 
      working group. For more information see the following web-page:

http://www.nothere.ukshells.co.uk/Iupac/wp%20project%20c.php?id=1

- Configuration (JobManager and DataManager)

- Preferences dialog

- In the Device Toolbar / JobExplorer box of the General page of the Preference dialog

the user can select whether the new Elements / JobExplorer toolbar (see below) is
      automatically closed when a Job is started in order to give the JobController window 
      more space on the screen.
  - Quantities/Units

- There is a new quantity -Fn (i.e. the negative value of the normal force) which is useful 
      for certain tack and texture analysis applications.

This quantity is calculated and saved by the Axial Ramp element only.

- There are two new quantities friction force Ff = M / R (with M ist torque, R is radius) and 
      friction coefficient m f = Ff / Fn for use with tribology measuring cell.

These quantities are calculated and saved by all the rotation elements, i.e. not by the 
      oscillation and axial elements.

- The units cm/s, mm/s and mm/s have been added for the quantity velocity. This quantity
      is used in the editor of the Axial Ramp Element.

- The unit of the inverse temperature quantity 1/T should be 1/K but was K in previous
      versions. This has been corrected.

- JobManager

- Main menu: Editor for Element.ini

- From the Help menu the user can launch an editor for modifying the Element.ini file 
      by selecting the Edit: Element.ini command.

- Main menu: Logfile Viewer

- From the Help menu the user can launch a viewer for the different log files that 
      RheoWin creates on demand:
         •  Rheowin.log : The general RheoWin log-file.

•  Rheometer communication log-files: e.g. Mars.log, RS600.log, ...

•  The diagnosis-file *.dia saved by the DeviceManager.

•  RhwException.log, VISAPI.log, DCAPI.log special log-files for debugging.
      Please note: For normal operation of RheoWin none of the above files are needed.

- Standard toolbar

- The icon for the Device Manager has been changed.

- Device toolbar

- The Device toolbar now has a button to reset the normal force signal to zero.

- The units for the gap, temperature and normal force display/edit fields are now 
      positioned similary.

- New combined Elements / JobExplorer toolbar

- The separate dialogs for selecting Elements and selecting Jobs have been replaced 
      by a completely new toolbar inside the main JobManager window with three pages;
      Elements, Job and Templates.

- The Elements page contains the elements for creating a Job by Drag&Drop, just like
      the Elements dialog in RheoWin 3.

- Both the Jobs page and the Template page contain an explorer tree structure which 
      only displays Job files (*.rwj) resp. Job template files (*.rwt) and sub-directories very 
      much like the Windows Explorer.

- The files and subdirectories displayed in the tree structures are identical to those 
      displayed in the Windows Explorer!
      Please note: Subdirectories NOT containing files of the corresponding type(s) are 
                           NOT shown in the tree structure.

- The default root directory of the explorer tree is displayed in the edit field above the 
      explorer tree and can be changed temporarily by clicking on the Select directory 
      button behind the edit field.

This functionality can disabled by removing the corresponding privilege in UserManager.
      Please note: The default root directory can only be changed permanently on the 
                           Directory page of the Preferences dialog in the Configuration menu.

- Files can moved between subdirectories by Drag&Drop.
      This functionality can disabled by removing the corresponding privilege in UserManager.
    - Files can be deleted by choosing Delete from the right-mouse-key popup-menu or 
      by clicking the Delete button at the bottom of the Job page in the toolbar. 
      This functionality can disabled by removing the corresponding privilege in UserManager.

- New folders (subdirectories) can be created by choosing New folder from the right- 
      mouse-key popup-menu or by clicking the New folder button at the bottom of the Job 
      page in the toolbar.
      This functionality can disabled by removing the corresponding privilege in UserManager

- New Goto-Element

- With the new Goto-Element loops can be "programmed" in a Job sequence. This is 
      usefull when creating Job in which a certain element sequence appears multiple times.
      In the Goto-Element, the element to jump to can be selected from a drop-down list. The
      elements are identified by a unique ID number (i.e. not by the position number in the 
      Job). The number of repetitions can be set.
      Please note: Currently the evaluation elements can not handle data from measuring
                           elements that are called more then once.

- File Load-Element and Reference-Element
    - Data in IUPAC XML file format can be imported using the normal File Open dialog
      and selecting a XML file (which must be in IUPAC format in order to be loaded).

- Message-Element

- With the new Repeat sound option on the Sound page of the element editor the user 
      can set the sound playback to be repeated until the Ok button of the screen message 
      text window is clicked.
      Please note: For the sound to be repeated the option Display message during Job
                           sequence must active also, otherwise there wouldn't be an Ok button 
                           to stop the sound playback.

- Set-Element

- The CR-Mode page in the element editor has been renamed to CR/CD-Mode since the 
      adaptable control loop parameters now also apply to the CD control loop. 
    - The CR/CD-Mode page for configuring the CR and CD adaptable control loop is now 
      also available for the RheoStress 600 and the RheoStress 6000.
      Please note: The adaptable CD and CR control loops are available in the following 
                           rheometer firmware versions (and in newer versions).
                           RS600   :  RS600-02_17_103-Dsp-10_06_000.h86

RS6000 :  RS6000-02_17_103-Dsp-10_06_000.h86

MARS   :  UPD_MARS_CBOX_12_04_005_Dsp_10_06_307.h86

- Temperature-Set-Element
    - The temperature page of the element editor has been modified and enhanced. The user
      can now select that the complete job will be discontinued when the set temperature is 
      not attained within a set tolerance after a set duration.

- New for (almost) all Measurement Elements

- On the Break criteria page of the Rotation page of the element editor the user can 
      now select Goto in the Action drop-down list. Once the Goto command is selected 
      a Goto button is displayed under the Action field. By clicking on the Goto button a 
      dialog is displayed from which the user can select an element of the Job to jump to
      when the break criteria is fulfilled.

Please note: In this version this functionality is still missing from 
                           the Temperature Set Element.
      Please note: This functionality will not be available in the MultiStep and

Creep-Recovery elements.

- All Oscillation Elements (not Multiwave Elements)

- The waiting time can now also be defined in seconds. The time in seconds can be 
      shorter than the duration of one period. 
      In the Frequency Sweep element the waiting time in seconds can also be set as a 
      maximum time when the waiting time is set as a number of periods, for example 
      "Wait for 5 periods but not longer than 10 s".
    - The oscillation elements have been optimized to achieve a more exact timing of the
      datapoints.

- The time passed while waiting for the set waiting time to be finished (at the start of the 
      element) is now included in the segment time. 
      Previously this time was erroneously added to the time between two segments.

- The time value for a data point is now the time at the end of the last oscillation period 
      that is used for one data point. Previously this was the time in the middle of all 
      oscillation periods used for one data point.

- The format of the oscillation raw data files (*.rwr) has been modified. A *.rwr files now 
      also contains all information neede to calculate the rheological values like G', G"
      etc. This new format is used by the modified *.RWR Viewer program (see below).

- Osc Time Curve, Osc Frequency Sweep and Osc Amplitude Sweep Elements

- Take from previous can now be used for taking the last set or measured stress or 
      strain value from the previous element as the set value for the current element.

- Osc Amplitude Sweep Element

- On the Acquisition page of the Oscillation page of the element editor a fixed 
      duration per step can now be set as an alternative to setting the number of repetitions.

During the measurement as many repetitions as will fit in the duration will be measured.
      Please note: The set frequency, i.e. the duration of one oscillation period, and the
                           duration per step must be given compatible values;

- Axial Ramp Element
    - The default setting on the Rotation page of the element editor is now CS-Mode, the 
      default stress/torque is 0.0.

- The new quantity -Fn (i.e. the negative value of the normal force) which is useful 
      for certain tack and texture analysis applications is now calculated and saved.

- DataManager

- Main menu: Editor for Element.ini

- From the Help menu the user can launch an editor for modifying the Element.ini file 
      by selecting the Edit: ELEMENT.INI command.

- Main menu: Logfile Viewer

- From the Help menu the user can launch a viewer for the different log files that 
      RheoWin creates.

- Standard toolbar

- In the standard toolbar there are two new (light green) icons Open last measurement 
      and Add last measurement for quickly opening the data file (*.rwd) of the last

measurement in a new page resp. adding the data file of the last measurement to the 
      currently active page.

- New  XML file import/export

- Data can be exported in the IUPAC XML file format with the new Save as (XML-IUPAC)
      command in the File menu.

- Data in IUPAC XML file format can be imported using the normal Open command 
      in the File menu and selecting a XML file (which must be in IUPAC format in order
      to be loaded).

- New  Data/Page/Template toolbar

- Inside the main DataManager window there is a completely new toolbar with three 
      pages: Data, Pages and Templates.

- Each of the three pages contains an explorer tree structure which displays Data files 
      (*.rwd), Page files (*.rwp) and Template files (*.gds, *.tds and *.rwl) respectively as

well sub-directories and files in subdirectories, very much like the Windows Explorer.

- The files and subdirectories displayed in the tree structures are identical to those 
      displayed in the Windows Explorer!
      Please note: Subdirectories NOT containing files of the corresponding type(s) are 
                           NOT shown in the tree structure.
    - From the Data explorer tree a Data file can be opened in a new page inside 
      DataManager by double clicking on the file or by selecting Open from the 
      right-mouse-key popup-menu or by clicking on the Open button at the bottom 
      of the page or or by dragging&dropping it on empty space inside the DataManager 
      or by dragging&dropping it on the title bar of the DataManager or highlighting the file 
      and pressing the Enter key on the keyboard.

- From the Data explorer tree a Data file can be opened in an already existing (open) 
      page inside DataManager by selecting Add from the right-mouse-key popup-menu or
      by dragging&dropping it on the title bar of an existing page.

- From the Page explorer tree a Page file can be opened inside DataManager by 
      double clicking on the file or by selecting Open from the right-mouse-key popup-menu
      or by clicking on the Open button at the bottom of the page or or by dragging&dropping 
      it on empty space inside the DataManager or by dragging&dropping it on the title bar 
      of the DataManager.

- A Page file can not be added to another page!

- The Template explorer tree basically consist of three independend trees: One for graph 
      templates, one for table templates and one for page templates.
    - From the Template explorer tree a Template can be applied to an existing (open) page
      inside DataManager by double clicking on the file or by selecting Open from the 
      right-mouse-key popup-menu.
      A graph template will be applied to the graph only, a table template to the table only 
      and a page template will be applied to complete page of the currently active page inside 
      DataManager.

- The default root directory of an explorer tree is displayed in the edit field above the 
      explorer tree and can be changed temporarily by clicking on the Select directory 
      button behind the edit field.

This functionality can disabled by removing the corresponding privilege in UserManager.
      Please note: The default root directory can only be changed permanently on the 
                           Directory page of the Preferences dialog in the Configuration menu.

- Files can moved between subdirectories by Drag&Drop.
      This functionality can disabled by removing the corresponding privilege in UserManager.
    - Files can be deleted by choosing Delete from the right-mouse-key popup-menu or 
      by clicking the Delete button at the bottom of the Job page in the toolbar. 
      This functionality can disabled by removing the corresponding privilege in UserManager.

- New folders (subdirectories) can be created by choosing New folder from the right- 
      mouse-key popup-menu or by clicking the New folder button at the bottom of the Job 
      page in the toolbar.
      This functionality can disabled by removing the corresponding privilege in UserManager

- Graph / Table display

- Table display

- All data values are now displayed in a normal font and not in a bold font anymore.

- *.RWR Viewer program

- The functionality of the *.rwr Viewer program has been significantly extended.

- The program now also displays the rheological quantities of the sample as numbers.

- In the rheological data graph the program now shows G' and G" as function of 
    frequency, time, stress, strain or temperature depending on the type of the first 
    segment in the data file.
  - By clicking on a data point in the rheological data graph the program will show the
    corresponding raw data information in the other graphs and numerical fields.

- "Walking" through the data points can be done by clicking on the buttons below the

numerical value display or by using the keyboard (left/right arrow key, home/end key, 
    page up/down key).

- By clicking on the right Y-axis (with the time on the X-axis) the user can select from a 
    popup menu which quantity to display on the right Y-axis.

- The program now shows the relative value of the 3rd and 5th harmonic of both the 
    stress and strain signal for each data point.

- After clicking on any of the four graphs with the right mouse button a menu will popup 
    which enables the user to print (on the default printer only), copy (to the clipboard) 
    or save (in an *.emf file) the graph.

- The program now shows the AngleRatio which is the ratio of the angle amplitude in the
    sample and the angle amplitude of the rheometer. This value is a measure for the amount
    of compliance correction applied. A value close to zero means that the compliance 
    correction is zero or very small. The smaller the value is the more compliance correction
    is applied.

- The program now shows the TorqueRatio wich is the ratio of the torque "lost" because 
    of instrument inertia and the effective torque applied to the sample.

2.2 Version 4.00.0001

Below is a list of bugs in RheoWin 4.00.0000 that are fixed in version 4.00.0001.

- Installation

- Language selection

- The language selected at the beginning of the installation was not transfered to the 
     language settings of RheoWin. This has been solved.

- Rheometer drivers

- Drivers for RS1, RO1, RS600 and RS6000

- On certain PCs on which RheoWin 3.xx worked without problems, RheoWin 4.00.0000
      produces "character overrun" and "framing error" communication errors. 
      This has been solved.

- Under certain circumstances (in combination with internal Jobs only) there was a problem
      reading sensor factors from the instrument. This has been solved.

- JobManager

- Osc Frequency Element

- Under certain circumstances an "Illegal value" error message would popup when closing 
      the Element-Editor. This has been solved.

- ROT Step Element

- This element crashed when the T set icon in the JobEditor was used to change the 
      temperature. This has been solved.

- ROT MultiStep Element, ROT CreepRecovery Element

- The T set icon functionality in the JobEditor did not work for these elements. 
      This has been solved.

- Area Calculation Element

- The area calculation did not work when the manual set data range was larger then the

actual range. This has been solved.

2.3 Version 4.00.0002

Below is a list of things that are new and/or changed in version 4.00.0002 compared with version 4.00.0001 of RheoWin.

- JobManager

- Set-Element

- The CR/CD-Mode page for configuring the CR and CD adaptable control loop is now 
      only available after installing RheoWin with a separate installatiion key. This means 
      that access to the CR and CD adaptable control loop is not part of  a standard 
      RheoWin installation.

2.4 Version 4.00.0003

Below is a list of things that are new and/or changed in version 4.00.0003 compared with version 4.00.0002 of RheoWin.

- General
  - Help file format
    - The help file format has been changed. This means that the help files are now compatible
      with Windows Vista without needing to install an update from MicroSoft.

- Rheometer drivers

- Driver for MARS
    - The optimize option for the number of repetitions per data points is now available for 
      the MARS.

Please note: The following MARS firmware (or newer) is needed for this work
                           UPD_MARS_CBOX_12_06_002_DSP_10_07_000.h86

- Driver for RV1

- On certain PCs on which RheoWin 3.xx worked without problems, RheoWin 4.00.000x
      produces "character overrun" and "framing error" communication errors. 
      This has been solved.

- Configuration (JobManager and DataManager)

- Quantities/Units

- The friction coefficient which was introduced in version 4.00.0000) was given a 
      wrong internal reference number, as a consequence the aT and bT shift-factors were not 
      available anymore. This has been solved.

- JobManager

- Oscillation Elements

- The optimize option for the number of repetitions per data points is now available for 
      the MARS.

Please note: The following MARS firmware (or newer) is needed for this work
                           UPD_MARS_CBOX_12_06_002_DSP_10_07_000.h86

- Reports

- New variable for reports

- A new variable VariableMeasureDeviceFullName is now available for display in a report. 
      This variable contains the complete original model name of a rheometer (which can not 
      be modified by a user).

2.5 Version 4.00.0004

(Released 19.11.2008)

Below is a list of things that are new and/or changed in version 4.00.0004 compared with version 4.00.0003 of RheoWin.

- Rheometer drivers

- Driver for F6/N6/F8/N8 circulators
    - Setting a temperature for these circulators was not possble when the unit symbol of
      the temperature was modified in RheoWin. This has been solved.
  - Driver for RheoStress 3000
    There is a dirver for the new RheoStress 3000 (which is only available in Japan).

- JobManager

- SetElement
    - A special help file is now available for the adapable CR/CD-Mode. The help file is opened 
      by clicking the Help button.

- MultiWave Oscillation Elements

- There was a problem with the timing of the MultiWave datapoints (since version 4.0). 
      This has been solved.

- Graph / Table display

- Table display

- In RheoWin 4 selecting a column in a table by clicking on the column header was not

possible anymore (this was possible in RheoWin 3). This functionality has been restored.

2.6 Version 4.00.0005

(Released 12.12.2008)

Below is a list of things that are new and/or changed in version 4.00.0005 compared with version 4.00.0004 of RheoWin.

- JobManager

- SetElement
    - The help file for the adapable CR/CD-Mode has been improved. It now offers integrated
      calculators to calculate the control loop parameters.

- SER Element

- The rheological values were not calculated correctly when the SER-tool was used in 
      CS-Mode. This has been corrected.

- Interpolation Element

- When using a user defined interpolation width (instead of the Default setting) the 
      software used the wrong equation which in the case of noisy data may lead to slightly
      wrong results. This has been solved.

2.7 Version 4.00.0006

(Released 04.03.2009)

Below is a list of things that are new and/or changed in version 4.00.0006 compared with version 4.00.0005 of RheoWin.

- Rheometer/Circulator drivers

- All devices
    - Under certain circumstances the communication between RheoWin and any 
      rheometers/viscometer was slowed down more or less (depending on which devices 
      were used) when RheoWin was communicating with multiple devices at the same. 
      This was noticeable when using a DC30 or DC50 circulator with any rheometer / 
      viscometer for example. This has been solved.

- Driver for DC30 and DC50 circulators
    - The communication routines for these two instrument have been optimized.  
  - Drivers for MARS, RS6000, RS3000, RS600, RS300, RS1 and RV1
    - Under certain circumstances the lift would not reach the set measurement position or 
      the set standby position but stop at a slightly larger or smaller gap. This mainly 
      happened when running measurements at higher temperatures. This has been solved.

- DeviceManager

- COM ports for DC30 and DC50
    - The user can now select COM1 to COM16 (instead of COM1 to COM4) for the 
      communication with a PC.

- Solid clamp measuring geometry
    - The user can now enter a value for the damping factor (for CR-Mode).

- JobManager

- Oscillation temperature ramp and temperature step elements

- The settings for the limiting maximum torque (checkbox and value) for CD-mode 
      were not properly saved when editing these elements in the JobEditor. 
      This has been solved.

2.8 Version 4.00.0007

(Released 23.06.2009)

Below is a list of things that are new and/or changed in version 4.00.0007 compared with version 4.00.0006 of RheoWin.

- DeviceManager

- Renaming devices

- In RheoWin 4.00.0006 renaming devices in the RheoWin DeviceManager was not 
      possible because of a bug. This has been solved.

2.9 Version 4.10.0000

(Released 25.08.2009)

- Installation

- Windows 7 compatibility

- The installation program has been modified to be compatible with Windows 7.
  - Template for spectra calculation

- The path for the default graph template for the spectra graph was set to an incorrect 
      value by the installation program. This has been solved.
  - New option interfacial rheometry

- In order to be able to use the new quantities and measuring geometries for interfacial 
     rheometry the new Interfacial Rheometry option (order no. 098-5057) must be installed.

- This option is automatically installed when using the installation key 098-5019 for all 
      instruments (this key is for Thermo internal use only).

- Measuring geometry selection

- By setting the option Manually select the measuring geometries (in the next three 
      windows) as the default option during the installation, the user is now guided to
      manually selecting which measuring geometries should be installed. This selection is 
      done in three subsequent dialog, one for "standard" parallel plate and cone and plate
      geometries, one for "standard" cylinder geometries, and for "special" geometries like 
      vanes, double cones, ER-geometries etc.

- New measuring geometries
    - The new measuring geometries with longer shafts which were developed for the 
      MARS III but who will replace the shorter geometries for all RheoStress and MARS 
      instruments are now part of the installation.

- General

- Program user interface style
    - The program user interface, i.e. the shape and colour of 'controls' (button etc.), has
      been modernized. 
  - Program startup

- When RheoWin is executed by a Windows user who does not have the rights to write 
      in certain directories (see the readme.doc file), RheoWin will now present the user a 
      clear and understandable error message.
  - Automatic program lock (for 21 CFR part 11 module)

- On the Security page of the Preferences dialog the RheoWin system administrator can 
      now define the duration of an inactivity (no mouse clicks, no use of the keyboard) interval
      in which RheoWin was not used. When this time interval is exceeded the control of 
      RheoWin is blocked until the user enters her/his login information again.
      Please note:  This functionality is only available when RheoWin is installed with
                            the 21 CFR Part 11 option!

- Language

- In RheoWin the word 'sensor' was used for referring to a measuring geometry, this has 
      been changed. 
      The word 'measuring geometry' is now used throughout the software instead.

- UserManager

- There are new per User(group) definable privileges for the Elements/Job/Template explorer
    (in JobManager) and the Data/Page/Template explorer (in DataManager) for:
     • Renaming files

- Rheometer/Circulators drivers

- MARS II, MARS III
    - Some improvement have been made in the TCP/IP communication.

- Several modifications were made to solve some time-out and instability problems.

- MARS III

- A new driver for the MARS III rheometer is now part of the installation.

- MTMC driver
    - A new driver for the MARS III Temperature Module Controller (MTMC) is now part of the 
      installation. This controller is an integral part of the MARS III.

- Rheostress 300, 600, 3000, 6000, MARS II, MARS III
    - MultiWave oscillation elements would not run directly after a normal oscillation 
      element. This has been solved.

- Stopping a MultiWave measurement did not work. This has been solved.

- Dynamax driver

- A new driver for the Dynamax circulator is now part of the installation.

- Simulator driver
    - The simulator now also supplies a random normal force "signal".

- DeviceManager

- Thermocontroller devices

- In order to make things clearer the Port, to which thermocontrollers that are integrated in 
      a rheometer (which is the case for the RotoVisco 1 and RheoStress 1) are connected, is 
      now called Internal (and not Remote anymore). The Remote connection is now only used 
      for external thermocontrollers that are connected directly to a rheometer (like the UTC).

- Brookfield measuring geometries
    - The Brookfield L1 to L4 and R1 to R7 measuring geometries can now be selected for 
      use with all RS, RT and MARS rheometers. With these geometries one can only 
      measure the viscosity of newtonian fluids.
      Please note: The values for the shear-rate and shear-stress that are calculated by
                           RheoWin using the supplied A- and M-factors should NOT be used!

- Measuring geometry types for interfacial rheometry

- In the dialog Properties of ... of the measuring there are two new options available for
      the type of measuring geometry; Interfacial ring and Interfacial bicone.

- One new measuring geometry with the name Du Noüy ring is installed when RheoWin

is installed with the Interfacial Rheometry option. 
      Please note: the user must enter the correct inner and outer diameter of the Du Noüy 
                           ring geometry and the fluid container combination before this geometry
                           can be used.

- The A- and M-factors of an Interfacial ring measuring geometry are automatically
      calculated when the diameter values are entered.

- Measuring geometries device list
    - In the box below the device list the inertia, compliance and expansion coefficient 
      are now also shown for the selected measuring geometry.

- Auxiliary devices

- The drivers for the Greisinger GMH 3110 and GMH 3111 manometers and the Ahlborn
      ALMEMO 2590-9 (and compatible units) hygrometer are now automatically installed and
      available in the auxiliary devices list in the DeviceManager.

- MSC calibration

- The MSC calibration routine has been optimized.

- The current absolute angle value is now displayed below the graph during the

calibration.

- By modifying the line
          ;MSCSpeed=0.01047

in the drivers.ini file the angular velocity with which the MSC calibration is performed 
      can be modified. This is an experimental function!
      The value in the above command is the angular speed in rad/s.

- Exporting MSC, MTC and TOT files

- The user is now asked to enter a filename when exporting these files.

- MARS II and MARS III firmware updater

- Some modifications have been made in order to be able to distinguish the MARS II and 
      MARS III.
    - For the MARS III a bootstrapsloader was integrated. This function is for qualified service 
      personal only!

- Configuration (JobManager and DataManager)

- Elements configuration dialog
    - In this dialog the user can select which element icons are displayed on the Elements page
      of the Elements / JobExplorer toolbar. 
      The settings are saved for each RheoWin user individually.

- Preferences dialog

- On the Directories page of this dialog the user can now define a base directory for the 
      Job, Data, Page and Templates sub-directories

- On the General page of this dialog the user can now set a font size for the text in the
      Information window. The selected font size is valid for the Information window in both 
      the JobManager and the DataManager.

- The default colour of the splitter has been changed to a light blue for better visibility.
  - Quantities/Units

- There is a new quantity vR, the circumfential velocity at radius R, for use with the tribology
      measuring cell and other friction related measurements.

This quantity is calculated and saved by all the rotation elements and by the 
      axial elements (i.e. not by oscillation elements).

- There is a new quantity We, the Weissenberg number, which is defined as the quotient 
      of the shear stress and the first normal stress difference. This quantity is calculated and 
      saved by all rotation elements.

- There is a new "quantity" Trigger, which can have the value 0 or 1 depending on whether 
       the trigger output signal is off or on.

- There are two new quantities Δh(t) = | h_trigger - h(t) | and Δ%h(t) =  Δh(t) / h_trigger 
      where h_trigger is the gap at the “trigger point” and h(t) the standard rheometer gap. 
      In RheoWin h_trigger is the "current gap" at the moment the first Axial-Ramp Element

in a Job is started.

This quantity is calculated and saved by the axial ramp element only .

- There are new quantities G'-i, G"-i, G*-i, J'-i, h-i, t-i, etc. with the proper units for
      interfacial rheometry.

- A new quantity group "Interfacial" has been added, this group contains all the special 
      quantities for interfacial rheometry.

- Symbol/Colour master layout dialog
    - In this new dialog the user can select the symbol and colour for every single quantity for 
      upto 32 data files. These symbol and colour settings are used as the default settings for 
      any graph in RheoWin when the option Use master layout on the Layout page of the 
      Data page of the Graph layout dialog is active.

- By double clicking on a column header above the table (in the new dialog) the symbol
      properties (shape, style, size, colour, etc.) for all quantities in one data file can be
      defined in the Layout dialog.

- By double clicking on a quantity in front of a row (in the new dialog) the symbol 
      properties for that quantity in all files can be defined in the Layout dialog.

- By double clicking on any symbol in the table the properties of that one symbol in on 
      data file can be defined in the Layout dialog.

- The settings made in the dialog can be stored in a (*.layout file) and loaded from 
      such a file.

- Two *.layout file are part of the RheoWin installation:
      In the file Master colour pro file, the files are distinguished by colour and the quantities 
      by symbol.

In the file Master colour pro quantity, the files are distinguished by symbol and the
      quantities by colour. This is the default setting after the installation.

- When a page which was created with a previous version of RheoWin is loaded (in 
      DataManager), RheoWin will always use the layout setting as defined in that page and 
      not use the colours and symbols defined in the master layout.

- JobManager

- Help menu in the Main Menu: Logfile-Viewer

- The Logfile-Viewer now also displays the log file from the e-mail program used 
      in the Message-Element.

- The Logfile-Viewer now also displays the *.err files written by the device drivers.

- Device toolbar

- In the Device Toolbar the user can now also directly set the temperature when a circulator
      or temperature control unit is connect to the rheometer or PC and when that unit is 
      selected as the default Thermocontroller on the New job default page of the preferences
      dialog in the configuration menu.
      Please note that there maybe a delay in opening and activating the Device Toolbar when
      JobManager starts up because some Thermocontrollers (mainly older circulators) have a
      slow communication interface.

- The functionality of the "LEDs" in the toolbar has been optimized: 
      After clicking the Go to gap or the Find and set zero point button, an orange "LED" will 
      blinking aside from that button until the action is completed, at that point the "LED" will
      become green. The green "LED" will disappear as soon as another button is clicked.
    - The timing of the data-acquisition of the toolbar has been optimized so that it does 
      not disturb the data-acquisition of a Job anymore.

- Elements/Jobs/Templates Explorer

- On the Elements page of this toolbar the individual element icons can now be made
      hidden (i.e. not visible and not accessible) by right-clicking on an element icon and
      selecting Hide this element from the popup-menu.

- Hidden Element icons can be made visible (and accessible) again using the Elements 
      configuration dialog. 
    - The Elements configuration dialog is be opened by right-clicking on any element icon 
      and selecting Elements configuration from the popup-menu. The
      Elements configuration dialog is also accessible from the Configuration menu.

- On the Jobs and Templates pages of this toolbar the job and template file names as 
      well as directory names can now be edited after a "slow double click" or by selecting
      Rename from the popup-menu (right-click), just like in the Windows Explorer.
      In the RheoWin UserManager each user can be denied to rename files by setting the 
      appropriate user privilege.

- On the Jobs and Templates pages of this toolbar the file and directory names can be 
      sorted forwards and backwards according the alphabet as well according to the 
      date/time of creation of the file by selecting the appropriate option from the Arrange 
      sub-menu on the popup-menu (right-click). 
      The selected sort order is saved and used until it is modified again.

- Job-Controller

- The large green Continue arrow with which the user can force the Job-Controller to 
       discontinue the current element and jump to the next element can now be disabled by 
       setting the appropriate user privilege in the RheoWin UserManager.

- Under certain circumstances there were some problems with the display of the 
       current temperature in the JobController window. This has been solved. 
    - The linear expansion coefficient of a measuring geometry is now always send to 
      the instrument at the beginning of a Job.

- Manual control / Monitor
    - The manual control window would crash when it was opened in the maximized state. 
      This has been solved.

- StartElement

- Messages about errors encountered when initializing the instrument are now more 
      informative.

- Set Element
    - The axial page in the Set-Element is now also available for all RheoStress 6000 and 
      RheoStress 600 with normal force option.

- The PID parameters of the RheoAdaptive control are now displayed in the JobEditor 
      and in the Information window in the JobController and in DataManager.

- Goto-Element

- The new Change temperature option can be used to automatically run one more or 
      measuring elements at a number of different temperatures in a comfortable way.

- No data saving in certain measurement elements
    - In the measuring elements listed below there now is an option NOT to save the data that 
      was acquired by that element. 
           ROT time curve, ROT ramp, ROT temperature ramp, 
           OSC time curve, OSC temperature ramp, 
           Axial time curve, Axial ramp.
      This is useful when a feature of a measurement element (like a break-criteria) is needed
      for meeting pre-test requirement without generating data points that are not needed.

- ROT and OSC Temperature Step Elements
    - The Set-Temperature value was not correctly saved under certain circumstances.
       This has been solved.

- Rotation Step Element
    - The minimum Step duration time for the Step mode option Fixed duration for each step 
      is now 0.1 seconds (instead of 1 second). 
      By using a Step duration time of 0.35 s and an Integration time of  0.15s, the Rotation 
      Step Element can now be used as a non-continuous "Ramp" which gives much better data 
      at low shear rates than the continuous (real) Ramp Element will give.
      The total time for this non-continuous Ramp must be calculated manually by multiplying 
      the time per data point (0.5 seconds in this example) by the number of data points. We 
      will offer a better solution for this in the near future.

- All Rotation Elements

- The Weissenberg number We, which is defined as the quotient of the shear stress and 
      the first normal stress difference, is now calculated and saved by all rotation elements.

- The new quantity vR, the circumferential velocity at radius R, is now measured and saved 
      by all rotation elements.

- All Oscillation Elements
    - The functionality of the STOP and NEXT buttons (in the JobController) has 
      been improved.

- The "Take from previous" option for the Auto tension force value (Axial page in 
      Element editors) did not work properly. This has been solved.

- Axial Ramp Element

- The end position of the ramp can now be defined as a percental value of the initial
      position of the ramp.

- The element now measures and saves the two new quantities Δh(t) and Δ%h(t). 
      These quantities can be used for texture analysis measurements.

- Axial Ramp Element

- On the Parameters page of the Axial page the dependence between the edit fields for 
      the Gap, Duration and Dh/t was not correct. This has been solved.
  - Axial Ramp Element & Axial Time Element

- The two quantities friction force Ff = M / R (with M is torque, R is radius) and 
      friction coefficient m f = Ff / Fn are now also measured and saved by the axial elements.

- The new quantity vR, the circumferential velocity at radius R, is now measured and saved 
      by the axial elements.

- The axial element now allows the acquisition of images from any compatible camera.

- Axial Time Element

- The quantities friction force Ff (CS-Mode) and circumferential velocity vR (CR-Mode) can 
      now be entered as a set value on the Rotation page of the editor of this element.

- Curve-Discussion Element

- For a calculated mean value there is a new QC criterium. The operator symbol for this

new criterium is ><. When this operator is selected an edit field for a percentual 
      value Y appears right of the operator selection box. 
      This criteria determines whether the calculated mean value differs more then Y % from
       the largest or smallest values in the data range. 
      This criterium can be used to check the amount of noise in a measured signal.

- Crossover Evaluation Element
    - The crossover element crashed when used in a Job when the measured data did not 
      contain a crossover point. This has been solved.
  - Yield-Stress Evalution Element

-  The calculation routines have been optimized.

- Creep/Recovery Evaluation Element
    - The subscript zero has been removed from the symbols for the calculated results.

- Thixotropy and Area Evaluation Element

- A mathematical bug in the calculation of the result has been removed.

- DataManager

- Opening files from the Windows Explorer
     - Double clicking on a *.rwd data file or a*.rwp page file will now also open this file in a
       new page in DataManager when DataManager is already running and already 
       contains pages. 
     - A *.rwd data file can be added to an existing page by dragging and dropping the file onto 
       the titlebar of that page. 
       Please note: Dragging a file on the inside of the page (i.e. on the graph or table) 
                            will NOT add the file to the page.

- File menu
     - With the new Save as without images command in the Save submenu a file which 
       originally contained images (from the RheoScope for example) can now be saved 
       without the images.

- In the dialog which appears when clicking the new Change file order command the 
      order of the currently loaded files (in a page) can be re-arranged using two arrow buttons.
      The file order is reflected in the graph legend and in the information window in a page.
    - The functionality to re-arrange the file order (see above) is also available in the Remove 
      file dialog.

- Standard toolbar

- The file order re-arange dialog is also opened by clicking on the new Change file order 
      icon in the standard toolbar.

- Data/Page/Template Explorer

- File name as well as directory names can now be edited after a "slow double click" or by
       selecting Rename from the popup-menu (right-click), just ilke in the Windows Explorer.
       In the RheoWin UserManager each user can be denied to rename files by setting the 
       appropriate User Privilige.

- File and directory names can be now sorted forwards and backwards according the 
       alphabet as well according to the date/time of creation of the file by selecting the
       appropriate option from the Arrange sub-menu on the popup-menu (right-click). 
       The selected sort order is saved and used until it modified again.
     - XML files (*.xml) are now listed in the explorer tree on the Date page.

- MWD calculation

- A mathematical bug which could lead to problems has been solved.

- Graph / Table display

- Data select for evaluation using the mouse
    - The range of data on which an evaluation will performed can now be selected by marking
      the first and last data point of the desired range in the graph using the mouse.

- In order to be able to use this new function it must enabled first, by either clicking on 
      the new Data select icon on the left-hand side of the status bar of the graph window 
      or by using the new command Range select > Active in the graph context popup-dialog 
      (right mouse click on graph).

- When this function is enabled the user can select a range by pulling-up a rectangle on 
      the graph (press right mouse button and keep it pressed while moving the mouse). 
      When the mouse button is released two red circles are drawn in the graph to mark the 
      first and last data point of the selected range.

- The range can also be selected by clicking on a datapoint and keep the (right) mouse 
      button down, then waiting for a fraction of a second for a red circle to be drawn around 
      the datapoint and then moving the mouse along the curve to any other data point while 
      keeping the mouse button down (and dragging a second red circle along the curve).
      When the mouse button is released two red circles are drawn in the graph to mark the 
      first and last data point of the selected range.

- As long as the two red circles are displayed in the graph they can be "grabbed" (with 
      the mouse) and moved along the curve to change the selected range.
    - By clicking on any other curve in the same graph, that curve will be selected using the 
      same x-range (the two red circles will mark the corresponding data points).

- By clicking on any other curve in the legend of a graph, that curve will be selected using 
      the same x-range (the two red circles will mark the corresponding data points).

- The range selected by the mouse is of course reflected in the Data select dialog, but 
      NOT (yet?) vice versa!

- The range selected by the mouse is of course reflected in the dialogs of the evaluation 
      elements (but modifications made in the selected range in the elements are NOT 
      transferred back to the graph).

- The selected range can be removed by clicking the Delete range icon on the left-hand
      side of the status bar of the graph window.
    - As long as this function is enabled, zooming in the graph using the mouse is disabled.

- The selected range is saved and restored when the graph is redrawn after opening

and closing the graph dialog, after rescaling, after adding/removing files, etc.

- After selecting a data range the user can open a small Calculated values tool

window by either right clicking on one of the two range markers and selecting

Calculate from the pop-up menu or by clicking on the C button in the status bar

of the graph.

While the Calculated values window is open the user can modify the selected range

by moving the range markers with the mouse, the calculated values will then be

re-calculated and updated.
      The Calculated values window currently shows the following values: x-range, y-range, 
       the mean y value with its standard deviation, the lin-lin slope, the log-lin slope and 
       the log-log slope.
      Selected calculated values can be transferred to clipboard and then pasted on to
       the graph.

- Graph layout dialog
    - On the Legend + text page of the Graph layout dialog the text which is displayed (for a 
      data file) in the graph legend can now be freely configured. The legend text can be a 
      combination of text fields like Filename, Substance name, Sample no, Comment etc. 
      as well a User-defined text.
      The user-defined text is stored in the data file and must be entered in the Identification /
      Notes dialog which can be accessed from the file menu or the standard toolbar.

- In the Masterlayout box on the Layout page of the Data page of the Graph layout dialog
      the user can (de-) activate the new Use master layout option. 
      When this option is active RheoWin will use the colours defined in the "Symbol/Colour 
      master layout" dialog in the Configuration menu and the controls to change symbols will 
      are disabled. In order to manually change any colour and/or symbol this option must 
      be deactivated.

- Graph legend

- The order in which file names are displayed in the graph legend can now be defined by 
      re-arranging the file order, see above.
    - The text which is displayed (for a data file) in the graph legend can now be configured, 
      see above.

- Proportional/Fixed text size

- Changing the text size option from proportional to fixed and vice versa now works 
       correctly on an active page.
  - Axis context menu

- By right clicking on an axis or the axis labels of an axis and then selecting Unit ... 
      from the popup menu the user can now select another unit for the quantity displayed 
      on the axis.

- When the right-mouse-key context-menu for an axis was used to change the number 
      format of that axis the scaling for the axis was set Autoscale. This has been solved.
  - Graph layout dialog
    - On the Legend + text page of the Graph layout dialog the text which is displayed (for a 
      data file) in the graph legend can now be freely configured. For the legend text the 
      Date and/or Time of the measurement can now be selected also.
  - Graph display
   - Some low level routines of the graph display functionality have been optimized 
      and debugged.

2.10 Version 4.10.0001

(Released 30.09.2009)

Below is a list of things that are new and/or changed in version 4.10.0001 compared with version 4.10.0000 of RheoWin.

- Installation

- MARS III installation

- The RheoAdaptive Control option (order no. 098-5056) is now automatically installed as 
      part of the MARS III installation. 
      Please note: This order no. is NOT shown on the installation welcome screen! 
                           (Only order no.'s for which the key was manually entered 
                            are displayed in that screen.)

- Rheometer/Circulators drivers

- MARS II, MARS III
    - Under certain circumstances (for example when the temperature is not yet constant)

the lift would never reach the Standby position (defined in a Lift-Element). This problem
      has been solved by giving the Standby position a default tolerance of 10 micrometer.
      The tolerance value can be modified by activating the following line in the drivers.ini file

[MARS2]
            ;LiftPosTolerance=0.025

The line is activated by removing the leading ";". In the example above the tolerance is
      set to 25 micrometer.

- JobManager

- Lift-Element

- Clicking on the green goto next element button in the JobController while the lift was
      moving to Standby position would end the Job completely. This has been solved.

- Curve-Discussion Element

- The QC value for the new >< operator was not displayed when this element was used 
      in a Job. This has been solved.

- DataManager

- Modifying the identification

- Modifying the Identification properties of a data file (sample name, legend text, etc.)

was not possible when the data file was initially loaded as part of a page (*.rwp, 
      page file). This has been solved.

2.11 Version 4.10.0002

(Released 09.10.2009)

Below is a list of things that are new and/or changed in version 4.10.0002 compared with version 4.10.0001 of RheoWin.

- Rheometer/Circulators drivers

- MARS III
    - In the manual control window the normal force value was intermittently not displayed 
      under certain circumstances. This has been solved.

- DeviceManager

- MTMC
    - On the right hand side of the MTMC diagnosis window the status of the temperature 
      control (active/not active) is now displayed.

- On the right hand side of the MTMC diagnosis window the status of the flow control

valves is now displayed. By opening the diagnosis window while a job (which includes

temperature control) is running, the status of the valves can be monitored on-line and 
      in  real-time..

- With the slider controls below the flow control valves the status of the valves can be 
      changed manually. Manually controlling the valves with the slider controls will stop the 
      control of the last set temperature!

2.12 Version 4.10.0003

(Released 03.11.2009)

Below is a list of things that are new and/or changed in version 4.10.0003 compared with version 4.10.0002 of RheoWin.

- JobManager

- Job-Editor

- It was possible to start a Job in which no measuring geometry was defined (selected). 
      Under certain circumstances this would result in the software sending a wrong 
      temperature value to the instrument.
      This has been solved. Starting a Job in which no measuring geometry is defined will 
      now result in an error message, and no commands will be send to the instrument.

- Oscillation Time Element

- The timing of the trigger function has been optimized.

2.13 Version 4.10.0004

(Released 10.11.2009)

Below is a list of things that are new and/or changed in version 4.10.0004 compared with version 4.10.0003 of RheoWin.

- Rheometer/Circulators drivers

- RS600
    - The RS600 driver which was part of the 4.10.0003 update had a problem regarding

oscillation measurements. This has been solved.

2.14 Version 4.10.0005

(Released 18.11.2009)

Below is a list of things that are new and/or changed in version 4.10.0005 compared with version 4.10.0004 of RheoWin.

- Installation

- Masterlayout files

- On deinstallation the Masterlayout settings are now saved. This means that during the

installation of the next new version, the Masterlayout settings will be restored 
      automatically when the "restore setting from previous version" is selected during

the installation.

Please note: In order to save the Masterlayout files of version 4.10.0004 or earlier you 
                           will have to make a copy of these files manually! 
      The *.layout files are by default stored in the following directory:

C:\Documents and Settings\All Users\Application Data\Thermo\RheoWin

- DeviceManager

- Measuring geometries

- The sample volume values for the following VT550 measuring geometries have been 
      modified: MV1, MV2, MV3, MV-DIN, MV-E, SV-DIN, SV-E, HV1, HV2
      These sample volume values were slightly wrong.

- The sample volume values for the following pressure cell measuring geometries have 
      been modified: PZ35, PZ36, PZ37, PZ38, PZ38 b, PZ39
      These sample volume values were slightly wrong.

- Since the sample volume values for the D75/300 Hasteloy pressure cell are slightly
      different the following new measuring geometry entries have been added to the list:
      PZ36 Ha, PZ38 Ha, PZ39 Ha

2.15 Version 4.10.0006

(Released 30.11.2009)

Below is a list of things that are new and/or changed in version 4.10.0006 compared with version 4.10.0005 of RheoWin.

- DeviceManager

- MTMC
    - The message Please select cooling media appeared when trying to set a temperature.
      This message should only appear when using the TM-EL-P, TM-EL-P + TM-EL-H or 
      TM-EL-C and when no Cooling media was yet selected on the Hardware page of the
      Properties of MTMC dialog.

This message should not appear when the TM-PE-P or TM-PE-P + TM-EL-H are used 
      since in this case the cooling media must always be a liquid (e.g. water).
      This has been solved.

- JobManager and DataManager

- Printing

- When using the Print command from the File menu in DataManager or the Print
      element in JobManager, long data tables sometimes were not printed completely 
      (some lines at the end of the table were missing). This has been solved.

2.16 Version 4.10.0007

(Released 11.01.2010)

Below is a list of things that are new and/or changed in version 4.10.0007 compared with version 4.10.0006 of RheoWin.

- Installation

- ART service program
    - The ART service program can now optionally be installed when a general RheoWin
      key is used for the installation. 
      Please note: The ART software is for use by authorized and trained service 
                           engineers only!

- Rheometer/Circulators drivers

- SC, AC and PC circulator
    - A new driver for the completely new range of Thermo Scientific circulators, consisting 
      of the Standard (SC), Advanced (AC) and Premium (PC) models is now part of the 
      installation.

Please note: The communication between a PC (i.e. RheoWin) and these new
                           circulators relies on a virtual COM port driver which causes these 
                           circulators (which have an USB interface) to appear as devices with 
                           a serial COM port.
                           This driver (FTDI USB driver) is available on the RheoWin CD and must 
                           be installed separately. 
                           Installation manuals are available on the RheoWin CD also.

2.17 Version 4.20.0000

(Released 02.07.2010)

Below is a list of things that are new and/or changed in version 4.20.0000 compared with version 4.10.0013 of RheoWin.

- Installation

- Symbol/color Master layout file

- The three default Symbol/color master layout files Master.layout, Master color pro 
      quantity.layout and Master color pro file.layout are now saved during the deinstallation 
      and restored during the installation when the option to use the settings from the 
      previous version is used.

- Per default the Master color pro quantity.layout file is now used in JobManager

and the Master color pro file.layout file is used in DataManager. When the option to 
      use the settings from the previous version is used during the installation, these 
      defaults are overwritten with the settings from the previous version.

- Measuring geometries for Peltier cylinder (TM-PE-C)

- The measuring geometries for the Peltier cylinder (TM-PE-C) are now part of the 
      installation.

- ART service program
    - The ART service program can now optionally be installed when a general RheoWin
      key is used for the installation. 
      Please note: The ART software is for use by authorized and trained service 
                           engineers only!

- General

- Splash screen

- Some of the images in the RheoWin start-up "splash-screen" have been updated.

- Language

- The language.xls file has been completely updated regarding the french and the 
      portugese language.

- A bug in the language.dll (i.e. the part of RheoWin which loads the language specific
      text from the language.xls file) was found and solved. Since this functionality is used 
      throughout RheoWin this bug fix may solve some "unexplicable" software problems.

- Number format: Decimal symbol

- RheoWin now uses the Windows settings (see the Windows Control Panel) for the 
      decimal symbol consequently throughout the software in all edit fields and for all 
      displayed numbers in graphs, tables, lists, etc. (apart from some export files, see below).
    - Depending on the Windows regional settings the decimal symbol may be a point (dot) 
      or a comma.

- For special export files like the *.MSC table files, *.MTC table file, *.TOT table files,
      *.RWR oscillation raw data files and *.ini files a point (dot) is always used as the
      decimal symbol for compatibility reasons.

- DeviceManager & Rheometer/Circulators drivers

- Main dialog

- The images on the buttons on the right hand side of the device list have been updated.

- MTC button

- In order to prevent problem arising from incorrect determined MTC tables, the MTC 
      calibration functionality is now hidden for normal users. Only qualified service 
      engineers should use this function.

- MSC dialog for MARS III
    - The text explaining the three "quality" options for the MSC calibration has been modified.
      The three options are now named: 
               High precision, duration ca. 20 min.
               Standard, duration ca. 10 min
               Fast, duration ca 5 min.

- All devices

- When the option Communication log is activated on the Options page of the device 
      property editor in DeviceManager, the user will now be asked whether this option should 
      be switched off or not every time the communication with the instrument is started.

This is to prevent that the communication logging is activated all the time.

- When a device was switched off while the communication between RheoWin and the 
      device was still running, it sometimes took a long time to actually stop the "broken 
      communication". The duration for this has been shortened.

- All rheometer and viscometer drivers
    - All drivers have been further optimized regarding fault tolerance and communication 
      speed.

- Under certain circumstances (for example when the temperature is not yet constant)

the lift would never reach the Standby position (defined in a Lift-Element). This problem
      has been solved by giving the Standby position a default tolerance of 10 micrometer.
      The tolerance value can be modified by activating the following line in the drivers.ini file

[rheometer_name]
            ;LiftPosTolerance=0.025

Where "rheometer_name" stands for rheometer driver *.dll name, like MARS2, MARS3,
        RS6000, RS1, etc.

The line is activated by removing the leading ";". In the example above the tolerance is
      set to 25 micrometer.

- MARS II and MARS III drivers

- After clicking on the new Set IPADR button on the General page of the Properties 
      of MARS dialog the user can now modify the IP adress of the instrument. 
      Currently this functionality is only available when RheoWin is already able to 
      communicate with the instrument. The MAC address dialog which appears when this

is not the case is not functional yet.
      Please note: This function should only be used by persons who know what 
                           they are doing!
      In most cases only the numbers after the last dot in the IP adress can be changed 
      without making the instrument inaccessible from the current PC! That means that

in the default IP adress 192.168.2.140 only the number 140 can be changed easily. 
      All other changes will need changes in the network setting of the PC also.
      The warning messages in the dialog in which the IP adress can be modified and in 
      the confirmation message boxes should be taken seriously.

- The above mentioned functionality for modifying the IP adress is also available in the 
      MARS II driver also, but in order for this work the bootloader firmware of the MARS 
      needs to be update first. Doing that is not trivial.

Documentation for this is available on request.

- The communication between the MARS and the PC has been improved regarding 
      continuity.

- The Scan function (to find a MARS in a Network) has been improved.

- Drivers for RT20, RS75, RS80, RS150, RS1, RO1, RS300, RS600, RS3000, 
    RS6000, MARS II and MARS III

- Under certain circumstances the CD-AS mode (AutoStrain) did not work properly 
      and did not reach the set strain value. This has been solved.

- Measuring geometries

- The damping value for the solid clamps is now set to 90 per default. With this setting a
       new CD-mode control loop in the MARS III which is optimized for the solid clamps is 
       activated.
       Please note: MARS III firmware DSP 50.06.000 or higher is need for this.

- MTMC and UTMC drivers

- The size of the temperature offset tables is now limited to 10 offset values due to

certain limitations in the firmware.

- MTMC driver
    - The display of the control status in the Diagnosis window has been corrected.

- The message "no cooling media selected" did not always appear when it was 
      appropriate. This has been solved.

- CTC (oven)

- The driver name, the type name and the device name of this device have been changed 
      from tc-oven.dll, OTC and TC-Oven to the correct names ctc.dll, CTC and CTC 
      respectively. This means that Jobs in which this device is used must be modified.

- The driver now works correctly with the MARS III.

- SC, AC and PC circulator
    - A new driver for the completely new range of Thermo Scientific circulators, consisting 
      of the Standard (SC), Advanced (AC) and Premium (PC) models is now part of the 
      installation.

Please note: The communication between a PC (i.e. RheoWin) and these new
                           circulators relies on a virtual COM port driver which causes these 
                           circulators (which have an USB interface) to appear as devices with 
                           a serial COM port.
                           This driver (FTDI USB driver) is available on the RheoWin CD and must 
                           be installed separately. 
                           Installation manuals are available on the RheoWin CD also.
  - External thermometer

- With a new driver (MultiTemp.dll) the Ahlborn ALMEMO 2590 universal meauring
      instrument (and compatible units) can now be used as a four channel thermometer.

- This driver is automatically installed and can be selected as Thermometer (Ahlborn 
      ALMEMO 2590) in the list of Auxiliary devices on the Additional data page of the 
      rheometer device editors in DeviceManager.

- The four measured temperature values are available as the quantities TxMT01, TxMT02, 
      TxMT03 and TxMT04 for display in all graphs and tables.

- Configuration (JobManager and DataManager)

- Preferences dialog

- The user can now set a default temperature value. This value will be used for any element 
      which is added to a Job in the JobEditor. 
      The user can also activated the Take from previous option for the temperature. When this

option is active this option will be activated in any element added to a Job.

- Some texts on the Security options page (21 CFR part 11 installation only) have been
      modified for easier understanding.

- On the General page in the Range select box the user can now select whether the 
      Range select per mouse function is active per default (instead of the Zoom function).
      Both the Range select per mouse and the Zoom function work by select a rectangular 
      area in a graph, so only one of them can be active at the same time.
    - On the General page in the Range select box the user can also select a colour for the
      two Range select markers.

- Symbol/Colour master layout dialog
    - The user can now select separate Master Layout files for the JobManager and the
      DataManager in the Configuration menu of each program.

- JobManager

- Element icons

- All element icons have been modernized. All measurement icons have a blue 
      background, all evaluation elements a green background and all general elements a
      light-grey background.
      The Goto, Set and Exec element icons have been slightly modified.

- JobEditor

- The text behind the icons in the element list is now displayed in a tabulated list which 
      also uses colour. 
    - The user can switch back to the old style element list display or disable the use of 
      colour by deactivating the corresponding options in the context popup-menu (to open 
      that menu click with the right mouse key on any element icon).

- The user can also change the font size of the element list from the context popup-menu.

- The above mentioned setting are stored and used for all Jobs displayed in the JobEditor.

- Manual control / Monitor
    - On the Numeric page of the manual control window the gap, normal force and 
      temperature values would sometimes change position. This has been solved.

- Automatic periodic saving of dating

- During a measurement (job) the acquired data is always saved in a temporary file 
      every 2 minutes, apart from in jobs in with images are acquired also. 
      This functionality can now be switched off in the File Save dialog.

- Lift element

- In the (slightly modified) editor of the lift element a user definable sample trimming 
      position can now be defined. When this option is activated the lift will stop at the

defined distance before the measurement postion while the rheometer drive motor 
      is locking the shaft so that the sample can be trimmed without rotating the 
      measuring geometry. A message will be displayed prompting the user to click Ok
      after finishing the sample trimming.

- The lift element now displays the Triming position (when activated) in 
       the Job-Editor list.

- The lift element now displays Standby position (when activated) in 
       the Job-Editor list.

- The Standby position now has a default tolerance band of 10 micrometer, see above.
  - Set element

- The zero point for the relative gap Δh and Δ%h can now be set. This is usefull for 
       texture analysis type of measurements.

- Setting a certain absolute angle has been made more accurate.

- All measurement elements

- All elements have been further optimized regarding fault tolerance.

- The icons on the set-parameter and data-acquisition-parameter pages have been 
       removed.

- Some changes in internal data calculations have been made to prevent strange 
       unmotivated crashes.

- Rotation ramp element
    - On the Parameter page of the Rotation page in the element editor the user can now
      choose between Continous and Stepwise for the ramp type.
          - In the case of a Continous ramp the shear-rate (CR-Mode) or shear-stress 
            (CS-Mode) is ramped up continously as smoothly as technically possible.
          - In the case of the new Stepwise ramp the shear-rate (CR-Mode) or shear-stress 
            (CS-Mode) is ramped up in discrete small steps.
    - In the case of a Stepwise ramp the data collected during the first half (but 
      maximally 1 s) of the step duration is discarded.
    - On the Acquisition page of the Rotation page in the element editor the user can now 
      enter a Integration time. This is the time during which raw data is collected. The mean
      value of this raw data is used to calculate the actual data points.
  - Oscillation time element

- The new FastOsc (Fast Oscillation) option is now accessible in the Osc Time 
      Element dialog when the firmware of the instrument (MARS III only) supports 
      this option.
      MARS III Firmware version 50.06.000 or newer is needed for this.

- When FastOsc in CS-Mode the torque can be defined using a table of 
       torque = f(time) values. This table can be calculated using a selection of functions 
       and by comparing the shape of the function with the result of a preliminary 
       measurement which was performed at constant torque value.

- The table can also be created manually (with an external editor) and loaded into 
       the Osc time element.

- Report element
    - When selecting a report template from the element editor the file open dialog will now 
      open the default report template directory unless the currently selected template was
      loaded from a different directory. In that case the file open dialog will open that directory.
  - Curve-Fit element

- Some potential division by zero cases have been removed.

- *.RWR Viewer program

- The *.rwr viewer program now contains two range bar indicators for the torque and angle.

- The *.rwr viewer program can now read *.rwr files from FastOsc measurements.

- The command Save continous sine wave data from the File menu can be used to 
     combine and save the individual sinewaves (1 period each) of all rheological 
     measurement points of a FastcOsc measurement into one file containing a continuous
     sinewave signal.

Please note: This (currently) only gives the correct result when the highest possible 
                          data acquisition-rate of 2 ms per data point is used in FastOsc.

- Graph / Table display

- New table function

- The table has been completely replaced by a modern up-to-date version.

- Tables can now be exported in Excel format directly (from the table context menu).

Excel files are saved with the *.xml extension and in the "Microsoft Office (Excel) XML 
      format". This format is compatible with Excel XP (or Excel 2002), Excel 2003 and 
      Excel 2007.

- DataManager

- Loading data iles

- The loading time for data *.rwd and page *.rwp files has been improved.

- Add text dialog

- The edit field for the text in the Add Text dialog has been increased in height from

two to four lines of text.

- Data select for evaluation using the mouse
    - The two (rather small) red circles who marked the selected range in the previous version 
      have been replaced by much larger markers which make it easier to move these 
      markers by clicking on them and dragging them to the desired position.

- Data select for evaluation using the data select dialog
    - Selecting the data range (data-file, quantity, X-axis range) for any evaluation routine 
      has been been made more comfortable.

- The data from the first loaded file and the first quantity found on the first Y-axis and 
      the first quantity found on the X-axis of the currently active graph (page) are now 
      automatically set a the selected data range.
    - The file selected in the result tree on the left hand side of a evalution dialog is now 
      automatically selected in the Data Select dialog also.

- In the Data Select dialog below the segment list, there are a now an All segments and
      a No segments button.

2.18 Version 4.20.0001

(Released 26.07.2010)

Below is a list of things that are new and/or changed in version 4.20.0001 compared with version 4.20.0000 of RheoWin.

- DeviceManager & Rheometer/Circulators drivers

- RS300, RS600, RS3000 and RS6000

- Certain additionally measured temperature signals from the UTMC were not saved when 
       the UTMC was connected directly to the rheometer (remote interface). 
       This has been solved.

- Universal Temperature Controller (UTC)

- The remote communication with MARS and RSxxxx rheometers has been optimized.

- Ahlborn ALMEMO thermometer

- On certain localized Windows versions (e.g. Japanese) the driver (MultiTemp.dll) for the
      Ahlborn ALMEMO 2590 universal measuring device did not work properly.
      This has been solved.

- JobManager

- All Rot elements

- Certain internal calculations needed to convert raw data to rheological could lead to 
      crashes under very special circumstances. This has been solved.

- Rot-Time, Rot-Multistep and SER element

- The automatic integration time in these elements did not work as intended. The
      integration time duration was not calculated correctly. This has been solved.

When the integration time is set to automatic (in CR-Mode only!) the integration time 
      is calculated according to the following equation:
          "Integration time" = 0.002 sec / Omega

Here Omega is the angular velocity in rad/s. The resulting (automatic) integration time
      is limited to 100 s.

- Osc-Time element

- When switching forth and back between the different modes the edit field for the max. 
      torque was not always enabled/disabled correctly. This has been solved.

- DataManager

- TTS module

- The TTS module in version 4.20.000 does not give correct results! This is caused by a 
      small omission (in this module) regarding the transition to using the Windows settings 
      for the decimal symbol. This has been solved.

- The dialog of this module has been modernized. Some text items have been changed.

- The new DataManager pages for the Shift factors, Shifted data and Master curve that 
      are created by the module to display the TTS results now have the corresponding titles
      in the title bar of the page windows (instead of titles like Page 2, Page 3 etc.).

- Spectrum module

- The Spectrum module in version 4.20.000 does not give correct results! This is caused 
      by a small omission (in this module) regarding the transition to using the Windows settings 
      for the decimal symbol. This has been solved.

- The dialog of this module has been modernized. Some text items have been changed.

- The new DataManager page for the Spectrum that is created by the module to display
       the Spectrum results now has a corresponding title in the title bar of the page window.

- MWD module

- The new DataManager page for the MWD that is created by the module to display
       the MWD results now has a corresponding title in the title bar of the page window.

- Graph / Table display

- New table function

- Under certain circumstances rows of data would not be displayed in the table during a 
      measurement (Job). This has been solved.

- When a value was deleted from a table using the Del key on the keyboard the 
      corresponding graph was not automatically updated.This has been solved.

- During a measurement (Job) the size of the table was not automatically adapted to the 
      size of the window when the window size was modified. This has been solved.

- When exporting to Excel the data index was not exported correctly (it started at 2
      instead of 1). This has been solved.

- Under Windows Vista and Windows 7 an exported ASCII or Excel file was not saved in 
      the correct directory. This has been solved.

2.19 Version 4.20.0002

(Released 28.07.2010)

Below is a list of things that are new and/or changed in version 4.20.0002 compared with version 4.20.0001 of RheoWin.

- DeviceManager

- Inertia determination

The inertia determination function did not work in version 4.20.0001. This has been solved.

- JobManager and DataManager

- Loading files under japanese Windows

When loading files under a japanese version of Windows, RheoWin 4.20.0000 "copied" the 
    data from the first file and used that for all subsequent loaded files when the path name 
    contained japanese characters. This has been solved.

2.20 Version 4.20.0003

(Released 24.08.2010)

Below is a list of things that are new and/or changed in version 4.20.0003 compared with version 4.20.0002 of RheoWin.

- DeviceManager & Rheometer/Circulators drivers

- RS1, RO1, RS300, RS600, RS3000, RS6000, MARS II and MARS III

- The file name format of the *.msc file which is automatically saved at the end of

the MSC calibration measurement was not uniform. This has been changed.

The file name now always contains the (short) name of the instrument plus the 
      date and time.

- Phoenix and Dynamax circulators

- The drivers for these circulators crashed when used in remote mode.

This has been solved.

- Auxiliary devices

- When an Auxiliary device was selected on the Additional data page of the
      Properties of ... dialog of a rheometer and when that auxiliary device was not

operational RheoWin would show wrong values for certain extra data channels
      like Hood-temperature etc. This has been solved.

- Image acquisition

- When an older version of the Matrox-Imaging-Library was installed on the PC (MIL 
      version <= 5) RheoWin would crash, this has been solved.

- Exporting *.msc files

- The number format of an exported measuring geometry MSC file was not correct.
      This has been solved.

- Graph / Table display

- Changing the quantity for a table columns

- Under certain circumstances changing the quantity for a certain column in a table did 
      not give the expected result: The quantity of another column as the selected colum

was changed. This has been solved.

2.21 Version 4.20.0004

(Released 19.10.2010)

Below is a list of things that are new and/or changed in version 4.20.0004 compared with version 4.20.0003 of RheoWin.

- JobManager

- Timing problem with data acquisition
    - In RheoWin 4.20.0002 and 4.20.0003 when a very high dasta acquisition rate was 
      used, data points would not get the correct time value. 
      This has been solved.

- Saving as ASCII
    - In RheoWin 4.20.000x saving as ASCII from a Job did not work. 
      This has been solved.

2.22 Version 4.20.0005

(Released 18.11.2010)

Below is a list of things that are new and/or changed in version 4.20.0005 compared with version 4.20.0004 of RheoWin.

- DeviceManager & Rheometer/Circulators drivers

- MARS III

- For the RheoScope module a lens with a magnification of 2.5x can now be selected.

- JobManager

- Data Export Element
    - Under certain circumstances using the Data Export element would lead to a software
      crash. This has been solved.

- Curve-Fit Element
    - Two new curve-fit equations have been added to the list of mathematical models.
      Slope log(y)=f(x) and Slope log(y)=f(log(x)). These curve fit equations can be used
      to calculate the log slope and log-log slope of (parts) of a curve. The slope is calculated 
      by means of a linear curve fit according to y = a + b*x through linearized data.
      As a result only b, that is the Slope value, is returned.

- DataManager

- Saving as Excel from a table
    - Saving as Excel was very slow. So slow that users got the expression that RheoWin
      was not working anymore when data was saved in an Excel file.
      This has been solved.

- Calculation popup dialog
    - Under certain circumstances (with negative values on the x-axis and after changing
      the selected range to include negativ x-values) the log(y)=f(x) slope and
      log(y)=f(log(x)) slope were not calculated correctly. This has been solved.

2.23 Version 4.30.0000

(Released 9.12.2010)

Below is a list of things that are new and/or changed in version 4.30.0000 compared with version 4.20.0005 of RheoWin.

- Installation

- Language file

- The Polish language column in the language file has been updated completely.

- Drivers and element for the Rheonaut module

- A new driver for the Rheonaut module is now part of the installation.

- A new driver for a FTIR spectrometer is now part of the installation.

- A new element for controlling the Rheonaut module and a FTIR spectrometer is 
     now part of the installation.
  - Driver for the Viscotester D and Viscotester E

- Two new drivers for the Viscotester D and Viscotester E are now part of the installation.

- DeviceManager

- Missing device drivers
    - When an instrument is listed in the devicemanger but the corresponding driver *.dll 
      is not installed, a clear message is now displayed in the box below the device list.
      The message is in red colour and shows exactly which driver is missing in 
      which directory.

- Driver for MARS III

- In the editor of the MARS III driver a 2nd MTC table (for the new low-torque mode) 
      can now be downloaded from the instrument.
  - Driver for the Viscotester D and Viscotester E

- Two new drivers for the Viscotester D and Viscotester E are now part of the installation.

- Driver for the Rheonaut module

- The new driver for the Rheonaut module is listed as thermocontroller in the RheoWin 
      DeviceManager.
      Using this driver RheoWin can control the temperature of the Rheonaut module and 
      control the axial position of the complete module relative to the rheometer drive 
      motor axis.

- Driver for FTIR spectrometer

- A new driver for a FTIR Spectrometer is listed as an auxilliary device in the RheoWin 
      DeviceManager. Using this driver RheoWin can communicate with the FTIR 
      spectrometer software. The driver is currently compatible with the Bruker Opus software.
      In the near future it will also be compatible with the Thermo (Nicolet) spectrometer 
      software.

- Driver for SC, AC and PC circulators

- A communication problems between these circulator and RheoWin was solved.
      Please note: For the communication to work without problems the circulator firmware
                          version 1.103 or newer is needed.

- The internal temperature ramp function of the AC and PC circulators does not work 
      when initiated using software commands. Because of that temperature ramps are now
      controlled by RheoWin, just like with the SC circulator.

- JobManager

- Element icons

- Some of the General-Element icons have been modernized.

- Elements configuration dialog

- The display of the element icons in this dialog was not correct. This has been solved.

- Job controller

- Error messages which come from devices (rheometer, viscometer, temperature 
      controller, circulator, AUX-devices) are no longer displayed in a messagebox (which 
      stopped the job sequence until it was closed) but in a new Events page in the Job
      controller window. This page is only shown when there are messages to be displayed.
      The page is automatically put in the foreground (this functionality can be deactivated).

The events that occured during a measurement are saved in the *.rwd data file.

- Identification Element
    - When in the identification element an item was marked as Disabled and Mandatory 
      at the same time AND that item is blank at run-time a Job containing this element 
      would not continue at this point. This has been solved, the Job can now be 
      cancelled using the Stop button in the Job-Controller.

- Goto Element

- In all previous RheoWin version the maximum number of elements in on Job was 
      limited to 499. This limit has been removed. The maximum number data segments 
      per data file was limited to 1024. That limit was removed also.

As a consequence the number of elements and resulting data segments is now 
      virtually unlimited.

Please note that due to a certain structural overhead in the element definitions a 
      Job with a very high number of elements needs a relative high amount of memory!

- Lift-Element

- The Trimming position option did not work properly when there was a Temperature 
      set element in the job sequence before the lift element. This has been solved.

- The Trimming position option did not work properly when the Thermo gap option 
      was active. This has been solved.

- Set-Element and Temperatur-Set Element
    - At the start of these elements any lift-control (i.e. normal force control or position

control) is now explicitely stopped in order to prevent problems with lift-control 
      functions set in previous elements.

- New FTIRSpectrum Element

- A new element for setting the parameters of the FTIR spectrometer software and for 
      setting the radial position of the Rheonaut module is now available.

- All non-MultiWave Osc Elements

- On the Parameters page of the editors of these elements the new Low torque option 
      can now be activated. When this option is active the torque resolution at very low 
      torques (< 100 nNm) is improved even further (the maximum torque is currently 
      limited to 3 Ncm when this option is active). 
     This option is available for the MARS III only.
      Please note: 
          1) For the Low torque mode to work MARS III firmware version 50.09.00x or 
              newer are needed.

2) The full effect of the Low torque improvements is only achieved with 
              instruments which were delivered with firmware versions 50.09.00x or newer 
              from the factory.

- Rot Time, Rot Stat. Flow Curve and Osc Time Elements

- These elements can now communicate with the Bruker Opus FTIR software in order 
      to simultaneously measure rheological data and FTIR spectra.

- Osc Temperature Ramp Element

- The FastOsc option (MARS III only) is now also available in the Osc temperature 
      ramp element.

- Under certain circumstances this element would not continue due to very rare data 
      format problems. This has been solved.

- Osc Time Element

- Due to a problem with the data transfer from a Rheometer to RheoWin this element 
      could crash under certain circumstances. This has been solved for all rheometers.

- All MultiWave Elements
    - The display of the torque and angle "sine-wave" (raw-data) was not correct.
      This has been solved.

- The multi-wave raw-data is now saved in the same format (*.rwr) as the normal 
      oscillation data. Please note that currently *.rwr files containing multiwave data can 
      not be loaded in the *.RWR Viewer, we are working on a solution.

- MultiWave Temperature Ramp Element
    - Due to a problem with the data transfer from a Rheometer to RheoWin this element 
      could crash under certain circumstances. This has been solved for all rheometers 
      which offer the MultiWave functionality.

- Curve-Fit Element

- Some potential causes for crashes (division bei zero) have been eliminated.

- DataManager

- Import of CaBER ASCII data

- When a *.cbr CaBER ASCII data file contains normal force data, this data is 
      now imported also.

- A corresponding graph template is now part of the installation.

- *.RWR Viewer
  - Sine wave data export

- Using the new command Export current datapoint sine wave data and Export all
      datapoints sine wave data in the File menu, the sine wave data of one selected
      rheological data point or the sine wave data of all rheological data point can be 
      exported to a separate ASCII file for each rheological data point.

2.24 Version 4.30.0001

(Released 15.02.2011)

Below is a list of things that are new and/or changed in version 4.30.0001 compared with version 4.30.0000 of RheoWin.

- DeviceManager

- Driver for MARS III

- The timing for the trigger signal in FastOsc mode was improved and is more accurate 
      now.

- The data acquisition routines have been improved. When using very high data aquisition
      rates the data display in RheoWin lagged under certain circumstances. This has been
      solved.

- In FastOsc mode and Rot mode (but not yet in normal Osc mode!) the trigger function
      can now provide a level signal or a pulsed signal.
      The Trigger mode can be set on the Options page of the Properties of MARS III dialog in
      the RheoWin Devicemanager.
  - Driver for the Viscotester D

- Some bugs in the driver for the Viscotester D have been removed.

- Driver for the Rheonaut module

- The Rheonaut module driver now also works in Remote mode.
    - In the device editor the Temperature Alarm settings have been disabled until
      further notice.

- The axial positioning control has been optimized.

- In the the Diagnosis dialog there now is a button for finding the zerop point of the
      axial positioning.

- MSC for measuring geometries

- When exporting the MSC table of a measuring geometry to a *.msc file, the
      selected path was ignored. This has been solved.

- Optimizing the MSC table of measuring geometry by running the MSC routine 
      a 2nd time using the Test of calibration option did not have any effect on the MSC table.
      This has been solved (for the instruments that support this function).

- JobManager

- Graph display settings

- When a job was loaded which was created using an older RheoWin version which did 
      not yet support the Master-Layout option, a manually defined graph definition was
      overwritten. This has been modified, the graph definition is now retained.

2.25 Version 4.30.0002

(Released 01.03.2011)

Below is a list of things that are new and/or changed in version 4.30.0002 compared with version 4.30.0001 of RheoWin.

- DeviceManager

- Driver for MARS III

- The handling of certain error messages coming from the instrument was not correct. 
      This has been solved.

- Under certain circumstances (for example after a lift-element) time values generated by 
      an oscillation element were wrong.
      This has been solved.

- Driver for MTMC (MARS III internal temperature controller)

- The handling of certain error messages coming from the instrument (error 34 amongst 
      others) was not correct. 
      This has been solved.

- Driver for SC AC and PC circulators

- The temperature offset value defined for these circulators were not used when sending 
      a set-temperature value to the circulator.
      This has been solved.
      Please note: As is the case with all other circulators that can be controlled by 
                         RheoWin the offset value is added to set-value, this means that on the 
                         circulator display the user will see the "modified" set value and the not 
                         the set value itself.
      An example: When the set temperature value in RheoWin is 20.0 °C and the offset 
                         value at that temperature 0.1 °C, the user will see 20.1 °C as the set 
                         value on the circulator display.

- JobManager

- Axial ramp element

- When the start value of an axial ramp was set as "current gap" (i.e. not  as a 
      predefined gap value) and the ramp speed was defined as the set parameter (instead 
      of the ramp duration), the set speed was ignored and the ramp duration was used
      instead. This has been solved.

2.26 Version 4.30.0004

(Released 14.03.2011)

Below is a list of things that are new and/or changed in version 4.30.0004 compared with version 4.30.0002 of RheoWin.

- DeviceManager

- Driver for RS150

- The inertia determination in RheoWin 4.30.000x did not work. This has been solved.

- Driver for RS300, RS600, RS3000

- The drivers for these instruments now recognize whether the lift is in a position where 
      only manual movement is allowed (for security reasons).
      Please note: The user will only notice this when the latest firmware is used.

- JobManager

- End element

- The error handling at the end of a job has been improved.

- DataManager

- Use layout from file

- The implementation of the Layout out of file when loading option on the General page 
      of the Preferences dialog (in the Configuration menu) has been optimized.
      When data which is saved by a Job using the Last segment only option (of the 
      Segments page of the Save data file element dialog) is loaded in DataManager, the last
      layout defined before that segment will now be used (instead of the last layout defined
      in the job).

- Reports
  - Report printout

- Under certain circumstances the graph in a report was printed using a very low resolution.
      This has been solved.

2.27 Version 4.30.0005

(Released 28.03.2011)

Below is a list of things that are new and/or changed in version 4.30.0005 compared with version 4.30.0004 of RheoWin.

- Installation

- New option FTIR spectroscopy (Rheonaut)

- In order to be able to use the Rheonaut module and a FTIR spectrometer in combination 
      with a MARS II oder MARS III the new FTIR Spectroscopy tool option (order no. 
      098-5061) must be installed.

- This option is automatically installed when using the installation key 098-5019 for all 
      instruments (this key is for Thermo internal use only).

- DeviceManager

- Driver for MARS III and Simulator

- Under certain circumstances the type of a selected auxiliary device was not 
      detected correctly. This has been solved.

2.28 Version 4.30.0007

(Released 18.04.2011)

Below is a list of things that are new and/or changed in version 4.30.0007 compared with version 4.30.0005 of RheoWin.

- DeviceManager

- Driver for Rheonaut

- The status information in the manual control dialog and the diagnosis dialog has been
      extended.

- Driver for IR Spectrometer

- RheoWin can now also communicate with the Thermo Scientific Nicolet Omnic 
      software which comes with Thermo Scientific Nicolet FTIR spectrometers.

- The spectrometer software is automatically started as soon as the MARS driver 
      communicates with the MARS instrument. This means that when the RheoWin device 
      toolbar is active when RheoWin starts up, the spectrometer software will be started 
      also. When the device toolbar is not active the spectrometer software will be started 
      when a Job is started, the manual control window is opened or when the diagnosis
      window is opened.
      Please note: RheoWin will never close the spectrometer software!

- JobManager

- Device Toolbar

- When a communication problem between the device toolbar and the rheometer occurs 
      the device toolbar will be now be closed automatically. This prevents problems with 
      the subsequent start of a Job or the manual control window.

- Manual control window

- The radial positioning of the Rheonaut module can be controlled manually from the 
      manual control window by clicking on the FTIR icon in the lower right corner of that 
      window.

Please note: In order for RheoWin to be able to control the Rheonaut module the
                         Rheonaut module controller must be set to Remote control (this is done 
                         on the front panel of the controller).

- FTIR spectrum element

- The part of the elment dialog which allows the user to set the radial position of the 
      Rheonaut module has been improved. The radial position can be defined relative to 
      the rim of the measuring geometry selected for the Job or relative to the center of the 
      of the measuring geometry.

- Alternatively the user can now select that a manual control window for setting the radial 
      position of the Rheonaut module will be shown during Job run.

Please note: In order for RheoWin to be able to control the Rheonaut module the
                         Rheonaut module controller must be set to Remote control (this is done 
                         on the front panel of the controller).

2.29 Version 4.30.0008

(Released 20.04.2011)

Below is a list of things that are new and/or changed in version 4.30.0008 compared with version 4.30.0007 of RheoWin.

- DeviceManager

- Drivers for RT20, RS75, RS80 and RS150

- A time-out in the communication with Remote connected devices (e.g. circulators) was 
      not handled correctly. This has been solved.

- JobManager

- Device Toolbar

- In version 4.30.0007 the Device Toolbar closed automatically directly after it was opened 
      when the correct default temperature control unit was selected . This has been solved.

2.30 Version 4.30.0009

(Released 02.05.2011)

Below is a list of things that are new and/or changed in version 4.30.0009 compared with version 4.30.0008 of RheoWin.

- DeviceManager

- Driver for Rheonaut module

- Some bugs regarding the radial positioning of the Rheonaut module have been solved.

- JobManager

- FTIR spectrum element

- Some cosmetical changes have been made in the element dialog.

2.31 Version 4.30.0010

(Released 12.05.2011)

Below is a list of things that are new and/or changed in version 4.30.0010 compared with version 4.30.0009 of RheoWin.

- DeviceManager

- Driver for FTIR spectrometer

- The automatically generated names for the spectra data files were not correct on a 
      PC with an english version of the Windows operating system. This has been solved.

- Driver for RS300, RS600, RS3000, RS6000

- The T_Pt100 temperature signal was not measured correctly. This has been solved.

- JobManager

- Yield-Stress Evaluation element

- By adding the line 
      [SPECIAL]

YieldStressCheckEndSlope=on
      to the elements.ini file, the automatic algorithm will work better with data which has 
      a sharp bend near the end of the curve. Normally this feature is not needed!

2.32 Version 4.30.0011

(Released 30.06.2011)

Below is a list of things that are new and/or changed in version 4.30.0011 compared with version 4.30.0010 of RheoWin.

- Installation

- Driver for the Viscotester D and Viscotester E

- The installation program did not use the correct key numbers for the
      Viscotester D and Viscotester E. This has been solved.

- DeviceManager

- Driver for RS6000

- Some modifications were made in the lift control. These modifications only have effect 
      when using firmware version 03.01.000 or newer.

- Driver for cameras (MARS II, MARS III and simulator only)

- RheoWin is now compatible with the following Foculus cameras from the company 
      NET GmbH (http://www.net-gmbh.com)

1) Foculus 323TB (monochrome camera)
      2) Foculus 323TC (colour camera)

3) Foculus 432TB (monochrome camera, upto 1280x960 pixel resolution only,
          i.e. the max. camera resolution of 1388x1044 is NOT supported)

- The format of the saved TIFF images has been (slightly) modified and should now be 
      compatible with all graphic software.

2.33 Version 4.30.0012

(Released 08.08.2011)

Below is a list of things that are new and/or changed in version 4.30.0012 compared with version 4.30.0011 of RheoWin.

- Installation & DeviceManager

- Driver for the SC and AC circulators

- Due to the fact that the new PC xxx circulators are not compatible with the driver for

the SC and AC circulators, the PC circulator is not listed anymore.
      Please note: RheoWin currently does not support the PCxxx circulators!

- Language file

- In the Japanese language column the text for the element names was not correct. 
      This has been corrected.

- JobManager

- Lift element

- ThermoGap can now also be activated for the Standby position. When ThermoGap is
      activated for the Standby position moving to that position maybe slower and the 
      position will be set without any tolerance.

- FTIR spectrum element

- The radial position of the Rheonaut module was not always stored correctly in the 
      data files. This has been solved.

- Axial ramp element
    - When an axial ramp element in which the lift speed is used as the set variable 
      was copied, the lift speed value was not copied. This has been solved.

2.34 Version 4.30.0013

(Released 19.08.2011)

Below is a list of things that are new and/or changed in version 4.30.0013 compared with version 4.30.0012 of RheoWin.

- DeviceManager

- Driver for MARS III, MARS II, RS6000, RS3000, RS600, RS300, RS1, RO1

- In certain situations the current gap value of the rheometer was not transfered correctly
      from the driver to the measurement elements. This could lead to spurious effects in the
      set shear rate value and deformation values..
      This has been solved.

- Driver for Rheonaut module

- Running temperature ramps did not work with the Rheonaut module.
      This has been solved.

2.35 Version 4.30.0014

(Released 21.09.2011)

Below is a list of things that are new and/or changed in version 4.30.0014 compared with version 4.30.0013 of RheoWin.

- DeviceManager

- Driver for RS6000, RS3000, RS600, RS300, RS1, RO1, RV1

- In version 4.30.0013 the value of the geometry gap was not displayed correctly in the
      information window. This error was only in the displayed value in the information window,
      i.e. the measured data as well as the gap value in the data are ok! 
      This has been solved.

- In certain situations using the log distribution in the ROT Ramp element would lead to 
      spurious communication problems. This has been solved.

2.36 Version 4.30.0015

(Released 10.11.2011)

Below is a list of things that are new and/or changed in version 4.30.0015 compared with version 4.30.0014 of RheoWin.

- DeviceManager

- Driver for SCxxx and AC xxx circulators
    - The driver for the SCxxx and ACxxx circulators is now compatible with both the old style 
      firmware (version numbers 1.10x) and the new style firmware (version number 095441.2B
      or newer).

Please note: Circulator firmware version 095441.2A is NOT compatible with RheoWin. 
                           When this firmware is detected by RheoWin a message will inform the user
                           to update the firmware. 
                           Updating the circulator firmware should be done by qualified personal only!

- Driver for MTMC (MARS III integrated temperature controller)

- RheoWin reported an error when trying to download the MTMC temperature offset values 
      when a TM-LI-C or TM-LI-P was connected to the MARS (MTMC). This has been solved.
      RheoWin now reports that for these two modules temperature offset value are not 
      available. Explanation: All TM-xx-x temperature offset values are write (set) offset values,
      since the TM-LI-C and TM-LI-P are passive modules, the actual temperature control is 
      performed by a circulator, so there are no write (set) offset values for the TM-LI-x.

- Reports

- A small change was made in the information transfer between RheoWin and the 
    List&Label report tool.

2.37 Version 4.30.0016

(Released 29.03.2012)

Below is a list of things that are new and/or changed in version 4.30.0016 compared with version 4.30.0015 of RheoWin.

- DeviceManager

- Driver for MARS III
    - The lowest frequency which can be used for the FastOsc mode is now 1e-5 Hz.

- The MARS III firmware has been modified in such a way that the lift can now always be 
      operated from RheoWin or the instrument front panel by clicking a lift control button or 
      a single button on the instrument front panel. This means that the lift message Manual 
      movement only will not popup anymore when the lift is in a "safety range". 
      This increase in control comfort has been realized by reducing the lift speed under 
      certain special circumstances, for example in the case of a MARS III with a mounted 
      CTC while using a TM-xx-x module.
      This new firmware also solves some other very special lift issues.

Please note: The following MARS III firmware versions are needed for this to take effect.
                           μP1 (RC-Box microcontroller)    50.13.000
                           μP2 (RC-Box DSP)                   50.12.000

μP3 (M-BoxTC microcontroller)  50.13.000

- JobManager

- Lift element

- The maximum value for the Standby position is now 120 mm.
  - Axial ramp element
    - When defining the Current gap as the start value for a ramp, the resulting End gap can 
      get a negative value during run-time. Since the Rheometer firmware does not accept 
      negative gap values this would lead to unexpected behaviour. 
      This has been solved, when the final gap value will be negative an error message will 
      now popup during Job run to inform the operator.
  - Curve-Fit Element

- The data segment selection as part of Job definition has been optimized.

2.38 Version 4.30.0020

(Released 24.05.2012)

Below is a list of things that are new and/or changed in version 4.30.0020 compared with version 4.30.0016 of RheoWin.

- JobManager

- ThermoGap
    - It was possbile to activate the ThermoGap function during a Job run by opening the 
      Manual Control window in a 2nd Job-Editor. Since this can have an undesired impact 
      on the running Job, this possibility has been dissabled.

- DeviceManager

- Measuring geometries
    - The default values of the torque correction values are now all set to 0.0

- The PZ DG 38 Ti geometry (double gap for pressure cell) has been added.

- Driver for MARS III
    - When the option Prompt message when finished on the Parameters page of the Axial 
      page of the Lift Element was activated the message was NOT displayed during the Job
      run and the Job would not continue at this point. This has been solved.

- Driver for F/N 6/8 circulators
    - Under certain circumstances the temperature values read from a F/N 6/8 circulator 
      were not correct. This has been solved.

- Reports

- In RheoWin version 4.30.0016 and 4.30.0015 the results of the Thixotropy analysis 
    routine were not correctly displayed in a report. This has been solved.

2.39 Version 4.30.0021

(Released 26.06.2012)

Below is a list of things that are new and/or changed in version 4.30.0021 compared with version 4.30.0020 of RheoWin.

- JobManager

- Lift-Element
    - Moving to Trim Position did not work properly with RV1, RS1 and RO1. 
      This has been solved.

- DataManager

- Graph layout dialog

- There was a problem on the Segments page of the Data page of the Graph layout dialog.

The segment selection was mixed up after switching to another page and back.
      This has been solved.

2.40 Version 4.30.0022

(Released 24.08.2012)

Below is a list of things that are new and/or changed in version 4.30.0022 compared with version 4.30.0021 of RheoWin.

- DeviceManager

- Driver for Rheonaut

- Some smaller modifications and bug-fixes were made in the Rheonaut driver.

- JobManager

- ROT and OSC temperature ramp elements
    - These elements can now communicate with the FTIR software in order 
      to simultaneously measure rheological data and FTIR spectra.

- Data Export element

- Exported ASCII files now do not contain empty lines at the end of the file anymore.

- DataManager

- Graph function

- The positioning of text on a graph has been improved.

2.41 Version 4.30.0023

(Released 11.10.2012)

Below is a list of things that are new and/or changed in version 4.30.0023 compared with version 4.30.0022 of RheoWin.

- DeviceManager

- Driver for MARS III

- New functionality for the new separate trigger box has been implemented.

- Driver for MTMC
    - Under certain circumstances the set temperature value was not correctly send to the
      MTMC. This has been solved.

- Driver for RS6000

- The MSC calibration routine is now identical to that of the MARS III. That means that 
      the MSC calibration can now be performed using one of 3 quality levels. The results of 
      a Test of Calibration run are now used to optimize the MSC calibration.
      A a result the low torque performance of the RS6000 can be improved.

- Driver for Rheonaut module

- The temperature limits of the Rheonaut modules have been changed to 0 °C - 120 °C 
       for the Peltier version and 20 °C - 400 °C for the electrical version.

- JobManager

- Identifikation element
    - This element now "remembers" the text entries for the Substance Name and Sample No. 
      These entries can be selected from the edit fields drop down lists.
  - Set element

- New functionality for the new separate trigger box has been implemented.

2.42 Version 4.30.0024

(Released 12.11.2012)

Below is a list of things that are new and/or changed in version 4.30.0024 compared with version 4.30.0023 of RheoWin.

- DeviceManager

- Driver for RS600

- A compatibility issue with the MSC table in an older firmware version was solved.

- JobManager
  - End of job
    - Under certain special circumstances a job could "hang" at the end of the job 
      after saving the data. This has been solved.

- Monitor window
    - After a time-out error message the monitor window could not be closed.
      This has been solved.
  - Curve fit element

- There was a problem with the Arrhenius_TTS_Lin curve-fit model. 
      This has been solved.

2.43 Version 4.30.0025

(Released 30.11.2012)

Below is a list of things that are new and/or changed in version 4.30.0025 compared with version 4.30.0024 of RheoWin.

- JobManager
  - Monitor window
    - The bug fixing in version 4.30.0024 introduced a new problem. 
       This has been solved.

2.44 Version 4.40.0003

(Released 25.01.2013)

Below is a list of things that are new and/or changed in version 4.40.0003 compared with version 4.30.0025 of RheoWin.

- Installation

- Upgrade installation or new installation

- The RheoWin installation program can now be run as an upgrade installation, that is 
      without deinstalling the previously installed version first, or as new installation. In the 
      last case a previously installed version must be deinstalled first. 
  - Upgrade installation

- When the settings of the previous installation are to be used used for the new 
      installation, the installation should be run as an upgrade installation, that is without
      deinstalling the previous version first. 
      Please note: The 'upgrade installation' method can only be used for an existing 
                           RheoWin 4.20.00xx or RheoWin 4.30.00xx installation! 
      Please note: For older RheoWin versions (version 4.10.00xx and older) the 'Upgrade 
                           installation' method can not be used, that means that the 'New
                           installation' method (see below) must be used, in this case the settings 
                           of the previous installation will not be available in the new installation.

- New installation

- When the settings of the previous installation should not be used used for the new 
      installation, the installation should be run as a new installation, in this case a previous 
      version must be de-installed first.

When there is no previous version installed, the installation is of course automatically 
      a new installation.

Please note: When deinstalling the previous version the settings of that version are 
                           deleted too and can not be retrieved.

- Entering installation key information

- Using copy and paste the complete key-code can you now be entered into the key

dialog in one action by selecting the first edit field and pasting the key-code into that
      field. The 4 blocks of the key-code are then automically entered into the 
      corresponding edit field. 
    - The complete key information (name, serial number and code) can now also be entered 
      by loading the *.txt key file using the Load Key button in the key dialog.

- Installation program

- A new version of the Installshield program is now used for the installation.

- General

- New development tool

- A new version of the development tool (compiler) is now used for creating RheoWin. 
      This will allow us to use modern Windows user interface controls, dialogs etc.in future
      versions. The new compiler solves some minor cosmetic problems in the previous 
      versions that occured when running RheoWin under Windows Vista, Windows 7 or
      Windows 8

- DeviceManager

- All devices
    - In a new date/time data channel with the name t_clock the date and time for each 
      data point is now saved. Currently this channel can only displayed in a table, that is 
      not in a graph.

- VTx measuring geometries

- The measuring geometries for the VTx are now split up into four Type categories named:
         Spindle L, R (Disc, cylinder),                                 [Geometries: L1 to L4 and R1 to R7]
         Spindle T (Bar, Helipath),                                       [Geometries: PA to PF]
         Spindle TL, TR (Cylinder, Small Sample Adapter)     [Geometries: TL5 to TL7 and TR8 to TR11]
         Spindle LCP (Cylinder, Low Viscosity Adapter)       [Geometries: LCP]
      This in order to be able to display the matching geometry information only.

Please note: The geometry types are not updated when the upgrade installation method 
                           is used. The user can manually select the correct new Type for each
                           geometry on the General page of the Properties of the geometry dialog
                           in the RheoWin DeviceManager.

- Plate and plate geometries

- The following plate and plate geometries have been added to the list of geometries: 
      P8 Ti L, P10 Ti L, P25 Ti L, P40 TI L, P50 Ti L.

- CCxxDIN Ti geometries

- The values for the axial gap were not correct, this has been corrected.
      The correct values are: 
             CC10 DIN Ti     2.113 mm
             CC16 DIN Ti     3.318 mm
             CC25 DIN Ti     5.300 mm
      Please note: These value are not updated when the upgrade installation method is used.

The user can manually enter the correct Distance values on the 
                           Geometry page of the Properties of the geometry dialog in the RheoWin 
                           DeviceManager

- CC27DG Ti geometry

- The value for the sample volume was not correct, this has been corrected.
      Please note: This value is not updated when the upgrade installation method is used.

- JobManager

- Device Toolbar
    - The device toolbar now contains a small new control which opens the New Job default
      page of the Preferences dialog directly.

- Elements, Jobs and Templates explorer
    - The Elements, Jobs and Template explorer is now based on the windows Panel Group
      Control instead of on the Page control for a more modern look.

- In previous RheoWin versions the complete file structure starting from the default Jobs 
      and Templates directories was scanned for RheoWin Jobs and Template files at the
      startup of the program. When these default directories contained many files 
      and/or were located on network directory, this scanning could take a rather long time.
      This has been solved, now only those directories of the file structure are scanned 
      which are currently opened in the Job and Templates file explorer.

- Load File Element
    - After activating the line

;LoadToFirstEvalHandleOnly = On        (remove the ; in front of the line)
        in the [ELMLOAD] section of the element.ini file. The Load File Element can now be 
        used to load multiple files (one after the other) in a looped Job which uses the 
        GoTo-Element. An example Job is part of the RheoWin installation.
        Please note: for normal use of the Load File Element this option must not be activated!

- Lift Element
    - When the Go to measurement postition option in the Measurement position group box 
      is selected, the operator can now select the new  Use current gap option (in the Lift 
      Element dialog). When this option is selected for a lift element which is placed "in the 
      middle" of a Job sequence, the lift will stay at the, at that time, current postion. 
      This can be used to activate the Thermo Gap option at a certain point in a Job.

- ROT Step Element (Stationary Flow Curve element)

- On the Options page of the element editor there is a new option Step duration + 
      integration time in rev. When this option is activated the values for Step duration and 
      Integration time on the Acquisition page of the Rotation page can be entered as a 
      number of revolutions. 
      The value for the Step duration must be larger as the value for the Integration time, the 
      two values can be set to 1.1 and 1.0 respectively for example.
      The minimum step duration time and the minimum integration time are set to 10 s 
      and 5 s per default. As a consequence for angular velocities above 6.0 rpm (6.0 rpm is 6
      revolution in 60 s, that is one revolution in 10 s) the step duration will always be 10 s and 
      the integration time 5 s as long as these two minimum values are not modified. 
      Please note: Allowing a too short step duration will result in spurious measurement data!
      Please note: This new option is only available for CR mode, with the Fixed duration for 
                           each step option as well as the Integration time option selected 
                           (on the Acquisition page).
    - On the Options page of the element editor there is a new option Save raw data. This 
      option is only available when the option Oscillation raw data on the Options page of the 
      Properties of "....." dialog for the selected rheometer is activated.
      When the Save raw data option is activated an ASCII file with the extension *.rwr and 
      the same name as the *.rwd data file will be saved. The *.rwr contains the time, 
      angle, angular velocity and torque values measured during the duration of this element as
      well the rheological data for each data point.
      The *.rwr file can be viewed with *.RWR Viewer.

- The option Show N1 has been moved to the Options page of the element editor.

- OSC Frequency Sweep Element

- For the number of Freq/Decade (frequencies pro decade) the user can now can select
      the additional (higher) values 14, 19, 39, 49 and 99.

- Creep Analyis Element

- In the new Numerical group box on the Layout page of the element editor the user 
      can now select which numerical values will be included in the result information text.

- There are four new result values available: The maximum strain and compliance values
      as well as the non-recoverable strain and compliance values, both as absolute and as
      percentual values.

- The result values are now displayed using the currently selected units.

- Graph / Table display

- Display of t_clock channel in tables

- For the new t_clock date/time data channel the format in which the date/time is

displayed in a table can be selected from the Format drop-down list on the Columns
      page of the Layout dialog.

- For the display of the data/time data several formats which include both the date and
      the time (like dd:mm:yyyy hh:mm:ss) as well as some formats which include the 
      time only (hh:mm:ss) are available.

- Display of t and t_seg channel in tables

- For the display of the measurement time channels t and t_seg several formats like 
      hh:mm:ss can now be selected from the Format drop-down list on the Columns page of 
      the Layout dialog.

- Resizing a table column width

- After resizing the width of a column, the table would always scroll down to the end

of the table instead of not scrolling at all. This has been solved.

- DataManager

- Data, Pages and Templates file explorer
    - The Data, Pages and Template explorer is now based on the windows Panel Group 
      Control instead of on the Page control for a more modern look.

- In previous RheoWin versions the complete file structure starting from the default Data, 
      Pages and Templates directories was scanned for RheoWin data, pages and template 
      files at the startup of the program. When these default directories contained many files 
      and/or were located on network directory, this scanning could take a rather long time.
      This has been solved, now only those directories of the file structure are scanned 
      which are currently opened in the Data, Pages and Templates file explorer.

- *.RWR Viewer

- The *.rwr viewer can now load a *.rwr file saved by the ROT Step Element and display 
    the data in a graph. 
    The graph can be zoomed by drawing up a (green) rectangle, starting
    with the upper left corner (!) of the rectangle, with the mouse (and while keeping the left 
    mouse keypressed). After releasing the left mouse button the graph will zoom to the 
    selected range.
    The graph scale can be restored by drawing up a (green) rectangle, starting with the lower 
    right corner (!) of the rectangle, with the mouse (and while keeping the left mouse key 
    pressed). After releasing the left mouse button the graph scaling will be restored.
    The graph can be panned (scrolled) by clicking (with the right mouse key) in the
    graph and moving the mouse while keeping the right mouse key pressed. This function 
    is especially useful after having zoomed the graph first.

- RangeCalculator

- With the completely new RangeCalculator the user can comfortably display and check
    the theoretical measurement range of any (technically possible) combination of 
    rheometer or viscometer plus measuring geometry.

Please note: The calculated and displayed range is the theoretical measurement range
                         which is defined by the torque and angular speed range of the rheometer
                         and the geometry factors of the measuring geometry. 
                         The practically useable measurement range will, in many cases, be 
                         smaller due to all kind of limiting factors like gap setting accuracy, 
                         sample filling issues, sample properties.

- Currently the measurement range is only available for rotation mode, i.e. not for 
    oscillation mode.

- The measurement range can be displayed as a graph of the viscosity as a function of 
    the shear-rate, as a graph of the shear-stress as a function of the shear-rate and as 
    numerical values.

- By entering a value for the Viscosity in the Reference sample group box the 
    (theoretically) useable range for this viscosity is displayed both graphically (a red line in
    the graphs) and numerically (red values).

- By clicking the Save as *.rwd button the calculated range values can be exported as a 
    RheoWin *.rwd data file. The *.rwd file contains the data points used to create the two 
    graphs mentioned above.

- By right clicking on any of the graphs, the graph can be printed (on the default printer), 
    copied (to the windows clipboard) or saved (as an .emf image file).

- By right clicking on the the numerical information text, the text can be printed (on the 
    default printer), copied (to the windows clipboard) or saved (as an .rtf text file).

- The RangeCalculator can be started in four different ways:
    1) From the JobEditor by clicking the icon in the upper left corner of the editor 
        window. In this case the rheometer and measuring geometry selected for the current 
        job are automatically used for the range calculation.
    2) From the DeviceManager by clicking the Range calculator button. In this case either 
        the selected rheometer or the selected measuring geometry in combination with the
        default rheometer is used for the range calculation.
    3) From the Programs menu in both JobManager and DataManager. In this case the 
        default rheometer and measuring geometry are used for the range calculation.
    4) Using the Windows Explorer and starting the program RHWRangeCalc.exe. In this 
        case the default rheometer and measuring geometry are used for the range 
        calculation.

2.45 Version 4.41.0000

(Released 02.08.2013)

Below is a list of things that are new and/or changed in version 4.41.0000 compared with version 4.40.0003 of RheoWin.

- Installation

- Version 4.40.0003 bugs

- The installation program of version 4.40.0003 contained a few smaller bugs, which 
      showed up under certain circumstances only. This has been solved.

- DeviceManager

- MARS II and MARS III
    - Under certain circumstances during a Job-run (measurement) the Temperature Set 
      Element would stop working an bring the Job to a halt when the Device Toolbar was 
      active during the Job-run. This has been solved.

- MARS III

- Under certain special circumstances the network scan function (for finding a MARS III 
      connected to the PC), would bring up an unreadable error message (when no MARS III 
      could be found). This has been solved.

- MTMC (MARS III build-in temperature control unit)
    - In the Offsets box on the Temperature page of the Properties of 'MTMC (MARSIII)' dialog 
      the user can now select between the default Automatic and three User defined 
      temperature offset tables.

Please note: The following MARS III or UTMC firmware version or newer are
                           needed for this to work.
                           MTMC (MARS III) : MBOXTC 50.13.121
                           UTMC                 : ?? (FW is under construction)

- When the Automatic option is selected, the MTMC firmware will automatically use the 
      correct temperature offset table for the TM-xx-x which is connected to the MARS III.  
      The table values, which are stored in the MTMC (MARS III) firmware for each TM-xx-x, 
      will be displayed in the table after clicking the Load from instrument button.
      (This is identical to the functionality in previous RheoWin versions.)

- When one of the three User defined temperature offset tables is selected, the MTMC 
      firmware will use that temperature offset table for any TM-xx-x which is connected to 
      the MARS III. The three User defined temperature offset tables are stored in the 
      MTMC (MARS III) firmware. The table values (of the currently selected User defined
      table) will be displayed in the table after clicking the Load from instrument button.

- The User defined temperature offset tables are designed to be used for TM-xx-x 
      setups that are NOT automatically recognized by the firmware. One example of such 
      a setup is the TMPxx adapter in combination with the TM-PE-C (Peltier Cylinder). For 
      this setup the (standard) temperature offset table of the TM-PE-C (for concentric cylinder 
      geometries) is not adequate.

- In order to be able to effectively use the User defined temperature offset tables a new 
      (second) instance of the MTMC should be created in the list of devices in the RheoWin
      DeviceManager. After renaming this new instance to MTMC (TM-PE-C + TMPxx), for 
      example, this new MTMC instance can be selected for and saved as part of a Job file.
      When this Job is then used, the User defined temperature offset table selected for 
      the MTMC instance used for this Job, will automatically be used.

- MARS III, MARS II, RS6000, RS3000, RS600, RS300, RS1 drivers

- The CD-AutoStrain control for the Frequency-Sweep element has been optimized
      (modified). Under certain circumstances the data of non-stationary sine-waves was used 
      for calculating the rheological datapoint. This has been solved. 
      Please note that as a result of this, the time needed to measure one data point maybe 
      longer than with previous RheoWin versions, as a result the time needed to complete a 
      Frequency-Sweep element may be longer than before, this may especially be the case 
      when the Frequency-Sweep runs from a lower to a higher frequency.
  - Rheonaut, FTIR data-acquisition

- The control of the FTIR data-acquisition has been optimized. 
    - By activating the new Send information option on the Options page of the Properties of 
      'FTIR Spectrometer' dialog (in the RheoWin DeviceManager) messages from the Omnic 
      software are now displayed in the JobController status box.
    - When the Stop button in the Job-Controller is clicked a StopCollect command is now send 
      to the Omnic software in order to allow for a controlled stop of the Job.
  - Driver for RS6000

- The driver for the RS6000 is now compatible with the updated version of the RS6000 
      (which is internally, see the diagnosis window, called RS6001).

- Interfacial rheometry

- The inertia and compliance values for the DuNoüy ring geometry have been added.

- The calculated value for M-factor of the DuNouy was not correct. 
      This has been solved.

- Greisinger manometer drivers
    - In previous RheoWin 4.40.00xx versions the driver for the Greisinger manometer did 
      not work. This has been solved.

- JobManager

- Closing JobManager
    - When the normal methods to close the JobManager do not work, the JobManager can 
      now be closed by clicking with the right mouse key in the empty area of the standard 
      toolbar (below the menu bar) while holding down the Ctrl + the Alt keys on the keyboard at 
      the same time.
    - Please note that under normal operation this new emergency stop method is not needed!

- Closing/stopping a running Job
    - A running Job can now be stopped by closing the Job-Editor window from which the Job 
      was started. After clicking on the [ x ] button in the upper right window of the Job-Editor, a 
      message-box with the text Job running! Close anyway will appear. When selecting Yes in 
      the message-box and after saving the data, the running Job will be stopped and the Job 
      windows closed.
    - When the Stop button in the Job-Controller does not react on a normal click on the button,
      a Job can now be stopped by clicking holding down the Ctrl + the Alt keys on the keyboard 
      and clicking the Stop button at the same time.
    - Please note that under normal operation these new emergency stop methods are not
      needed!

- Identification / Notes Element

- On the Substance page of the element editor the stored entries for the Name and 
      Sample no can now be deleted by right clicking (with the mouse keys) anywhere in 
      the dialog (but not on any dialog text or edit field) and selecting the appropriate item 
      from the popup menu.

- Save Element
    - In version 4.40.0003 the generation of an automatic file name (for a data file) according
      to certain rules did not work properly. This has been solved.

- Camera Element

- The controls for the RheoScope module are now only displayed when the RheoScope 
      module is actually connected to the MARS. When this is not the case, i.e. when a 
      camera is used without the RheoScope module, these controls are not displayed.

- All measurement Elements
    - The RangeCalculator can now also be opened by right clicking (with the mouse keys)  
      anywhere in an element editor dialog (but not on any dialog text or edit field) and 
      selecting the Information item from the popup menu.

- ROT Time Element
    - In the new  In case of gap change box on the Options page of the element editor, 
      the user can can now select between the new options Keep angular velocity constant 
      and Keep shear rate constant. 
      When using a parallel plate measuring geometry, and with the option Keep shear rate 
      constant active, the angular velocity will automatically be adapted, when the gap 
      changes, in order to keep the shear contant.
      The default setting is Keep angular velocity constant, since this method was used 
      in all previous RheoWin versions.

Please note: This is available for the MARS II and MARS III only.

- OSC Frequency Sweep element

- The CD-AutoStrain control for the Frequency-Sweep element has been optimized 
      (modified). See above for more details.
  - MultiStep Element

- In the MultiStep Element upto 60 different steps can now be defined. 
      Please note: The following MARS II or MARS III firmware versions or newer are
                           needed for this to work.
                           MARS II : CBOX 13.01.004 DSP 10.10.008
                           MARS III : RCBOX1 50.14.017 DSP 50.13.002

- Multiple steps can now be selected for Copy, Paste and Delete by using the left 
      mouse key in combination with the Ctrl and Shift keys on the keyboard.

- With the new Copy and Paste buttons one or multiple steps can now be copied and 
      pasted in to the list of steps at any position.

- With the Delete button multiple steps can now be deleted at the same time.

- With the new Copy last 2 steps and insert 9x button the last two steps are copied 
      and inserted 9 times at the end of the list. 
      This function is meant to be used for quickly creating a job for the so-called MSCR 
      (Multiple Stress Creep Recovery) experiment which consists of 40 or 60 steps in total.
    - When clicking on the Duration and # data point step table headers a new dialog will 
      open in which the duration and the number of data points for all even and all odd steps,

or for all steps can be changed at the same time.

- Axial Ramp Element

- When the value zero was entered in the Dh/t edit field on the Parameter page of 
      the Axial page of the element editor, the editor would crash. This has been solved.

- JobManager and DataManager

- Viewing the new.doc and readme.doc documents
    - The new.doc (that is this document) and the readme.doc documents can now be opened
      directly from within RheoWin using the Readme command in the Help menu.

- Creep-Analyis Element

- The settings of the items in the Numerical group box on the Layout page of the 
      element editor (which were introduced in version 4.40.0003) can now be saved by
      clicking the the new  Save button. The saved default settings are used in both the 
      JobManager and the DataManager for every new Creep-Analysis calculation.
  - Cross-Over Element

- In the new Numerical group box on the Layout page of the element editor the user 
      can now select which numerical values (G', G", f, etc.) will be included in the result 
      information text.

- There are four new result values available: The complex viscosity (eta*) and the 
      complex modulus (G*) as well as both viscosity values (eta' and eta").

- The result values are displayed using the currently selected units.

- The settings of the items in the Numerical group box can be saved by clicking 
      the new  Save button. The saved default settings are used in both the JobManager 
      and the DataManager for every new Cross-Over calculation.
  - Curve-Fit Element

- In the new Numerical group box on the Layout page of the element editor the user 
      can now configure the result information text:
      The user can select whether the model name, the equation, the physical units of the
      calculated model parameters, the value of chi2, the value of the regression 
      coefficient r and the physical units of the X- and Y- axis quantities should be displayed
      as part of the result text or not.

- For the display of the physical units of the calculated model parameters, the currently 
      selected units are used (i.e. the same unit as used for the axis scaling).

- The settings of the items in the Numerical group box can be saved by clicking 
      the new  Save button. The saved default settings are used in both the JobManager 
      and the DataManager for every new Curve-Fit calculation.
  - Curve Discussion Element

- Under certain circumstances this element would show error messages. 
      This has been solved by a temporary bug fix.

- Graph / Table display

- Axis scaling

- Under certain circumstances the axis scaling routines would not work properly, under very 
      special circumstances this could lead to RheoWin crashing. This has been solved.

- Display of axis titles

- Under certain circumstances the position of the axis titles was not correct (i.e. not
      centered). This has been solved.

- Under certain circumstances vertical axis titles were unreadable when running under 
      Windows 7. This has been solved.

- Moving the legend

- When the legend was moved on the graph (using the mouse), the box indicating 
      the size of the legend during the moving jumped to a slightly different position after
      releasing the mouse button. This has been solved.

- Size of a table

- Under certain circumstances a table would not fill out its assigned space.
      This has been solved.
  - Display of t_clock channel in tables

- The time value in the t_clock channel was wrong by exactly two hours.
      This has been solved.

2.46 Version 4.41.0006

(Released 18.12.2013)

Below is a list of things that are new and/or changed in version 4.41.0006 compared with version 4.41.0000 of RheoWin.

- Installation

- Installation key dialog
    - Under certain circumstances the cursor would move by itself. This has been solved.

- DeviceManager

- Simulator
    - The reset time function in the simulator driver did not work correctly. 
      This has been solved.

- Measuring geometries

- In the editor for the measuring geometries some edit fields were too short. 
      This has been solved.
  - MSC calibration
    - There was a problem when saving the MSC values at the end of the MSC calibration. 
      This has been solved.
  - Inertia, MSC and MTC calibration
    - The animated status display graphic did not work correctly. This has been solved.

- JobManager

- Screensaver

- During any Job in which FTIR spectra are collected the Windows Screensaver is now
      disabled.
    - The Windows Screensaver can be manually disabled by clicking on the RheoWin 
      JobManager's main-window status-bar with the right mouse key.

- Manual control
    - The manual control dialog has been optimized to prevent it from crashing/stop working.
  - JobController
    - Under certain circumstances the error message "falsche Beschreiberklasse" would 
      pop-up. This has been solved.

- Export Element
    - In the Element Editor the pathes for the Excel and PDF report templates were not set to 
      the default RheoWin pathes. This has been solved.

- In the File select dialog that is opened when selecting a new template, the path to the 
      currently selected template is set as the initial path.

- All measuring Elements with a second raw data graph
    - There was a scaling problem in the second graph (for the raw data). 
      This has been solved.
  - Curve Fit Element
    - Under certain circumstances a curve fit would crash. This has been solved by 
       increasing the calculation accuracy.
    - The Polynom and Tscheussner models have been optimized.
  - Curve Discussion Element
    - Under certain circumstances a maxiumum would not be calculated correctly. 
      This has been solved been increasing the calculation accuracy.

- JobManager/DataManager
  - Saving camera images
    - Under certain circumstances there were problems when saving LWF, TIFF or AVI files.
      This has been solved.

- Graph / Table display
  - Table -> graph interaction during a measurement
    - When a value in the table is entered/changed during a measurement (Job run or Manual 
      control), the graphic display of the data will now be updated automatically accordingly.

- Layout / Save dialogs
    - Layout and save dialogs are now always opened on top of all other dialog.
    - Layout and save dialogs do not appear in the windows taskbar anymore.

- Marker lines

- Under certain circumstances error messages would pop-up when marker lines 
      were drawn. This has been solved.

2.47 Version 4.41.0019

(Released 16.04.2014)

Below is a list of things that are new and/or changed in version 4.41.0019 compared with version 4.41.0006 of RheoWin.

- Installation

- Viscotester iQ
    - The installation program now allows the installation of RheoWin for the new Viscotester iQ
       rheometer.

- DeviceManager

- Drivers for Viscotester iQ
    - There are two new drivers for the new Viscotester iQ.
      The VTiQ.dll driver for controlling the Viscotester iQ itself
      The VTiQT.dll driver for controlling the Viscotester iQ integrated electronics for the 
      optional TM-PE-C (Peltier Cylinder) temperature control module.

- Driver for RS3000

- The driver for the RS3000 is now compatible with the updated version of the RS3000 
      (which is internally, see the diagnosis window, called RS3001).

- MSC calibration RS3000
    - There was a problem when saving the MSC values at the end of the MSC calibration. 
      This has been solved.

- JobManager

- JobController
    - When a Job is cancelled during the initialisation phase (before any data was acquired), the
      File Save dialog will not popup any more.
  - All measurement elements and the temperature set element
    - The temperature set values are now checked against the allowed min/max temperature 
      values at the start of Job (and not only during the editing of a Job). When the allowed
      min/max temperatures are exceeded a message will popup and the Job will be cancelled.

- ROT Ramp Element Editor
    - When the edit field for the ramp duration was empty (during editing) the editor would 
      crash. This has been solved.

- All OSC Elements

- The logic for saving images in relation to the rheological datapoints of OSC elements has
      been changed.

- Graph / Table display
  - Layout dialog
    - Under certain circumstances the Graph and the Table layout dialogs would cause
      crashes. This has been solved.
  - Saving a graph as a bitmap
     - Under certain circumstances saving a graph as a bitmap file did not work. 
       This has been solved.

2.48 Version 4.50.0003

(Released 24.07.2014)

Below is a list of things that are new and/or changed in version 4.50.0003 compared with 
version 4.41.0019 of RheoWin.

- Installation & RheoWin Startup window

- Viscotester iQ
    - The image of the Viscotester 550 in the installation routine dialogs and in the RheoWin
      startup window (splashscreen) has been replaced by that of the new Viscotester iQ.

- DeviceManager

- Driver for RheoScope 1

- There was a problem with the microscope's radial position and focus values. 
      This has been solved.

- Drivers for Viscotester iQ
    - The driver for the Viscotester iQ is now compatible with the upcoming Viscotester iQ 
      oscillation mode.

- Driver for FOculus cameras
    - RheoWin is now also compatible with the new FGControl software and drivers for the
      (RheoScope) FOculus 323TB and 323TC cameras.

- With the new FGControl software and drivers the FOculus cameras can now be used with 
      RheoWin under the Windows 7 32-bit and 64-bit operating system.

Please note: See the separate "HAAKE RheoWin - Camera driver installation" 
                           instructions on how to properly install the FGControl software and drivers
                           for Windows 32-bit and 64-bit operating systems.

- Driver for Sony camera

- In order for the Sony XCD-X710 camera to work with RheoWin a small update needs to 
      be performed after installing RheoWin. The driver for the Sony camera is only compatible 
      with Windows XP 32-bit.

Please note: See the separate "HAAKE RheoWin - Camera driver installation"
                           instructions on how to apply this update.

- Many rheometer and temperature control device drivers

- The Apply button on the Temperature pages of the "Properties of ..." device dialog is now 
      active when changes were made on these pages.

- JobManager

- Device toolbar
    - The device tool bar caused problems with the image acquisition (e.g. RheoScope module) 
      when it was active during a Job (measurement). This has been solved.

- Manual control / Monitor
    - The button for the camera control in the Manual Control / Monitor window is now only 
      active when the initialization process of the instrument is completely finished.

- All measurement elements
    - There is a new quantity or data channel t_meas in which the time measured starting from 
      the start of the first measurement element is saved.

- There is a new quantity or data channel User defined in which the value of a special user 
      defined quantity can be stored. This quantity can be given any symbol (or name) and 
      any unit.

- Show data window Element
    - The Show data window element now has an new editor dialog in which the following 
      settings can be made:
      - Show large (green arrow) next button in JobController

When this option is activated a large button with a green arrow and the text Next on it is 
        displayed in the JobController. After Clicking the next button the Job will continue with the 
        next element.
      - Deactivate time reset in device at job start
        When this option is activated the time measured by the device (rheometer) will NOT be
        reset at the start of the Job. This option should only be activated when running several 
        Jobs in parallel with one device. In that case the option must be activated for all Jobs 
        apart from the Job that is started first.

- Deactivate communication with device at start of this element

When this option is activated the communication between RheoWin and the device 
        (rheometer) is deactivated at the start of the element. This allows another Job to 
        communicate with the device while this Job is pausing.
      - Show edit field for User defined variable in JobController

When this option is activated an edit field for entering the value of the User defined 
        variabele is displayed in the JobController.
      - Reactivate communication with device at end of this element

When this option is activated the communication between RheoWin and the device 
        (rheometer) is reactivated at the end of the element, that is after clicking the small or 
        large (green arrow) Next button.
  - ROT Step Element (Stationary Flow Curve element)

- On the Options page of the element editor there is a new option Step duration + 
      integration time as inverse of shear-rate. When this option is activated the values for the 
      Step duration and the Integration time on the Acquisition page of the Rotation page are 
      defined as a multiple value of the inverse value of the shear rate.

For example: At a shear of 0.1 1/s the step duration will be 10 s when the multiplication 
      factor is set to 1.0 and 30 s when the multiplication factor is set to 3. 
      Since the integration time is part of the step duration, the value for the Step duration must 
      be larger than the value for the Integration time.

When the resulting step duration and integration time values are smaller than the values 
      defined for the  minimum step duration time and the minimum integration time, these  
      minimum values are used. 
      For example: At a shear rate of 10 1/s the inverse value (which is 0.1 s) is smaller than the  
      minimum step duration, therefore the step duration will be set to 1 s. 
      The default values for the minimum step duration time and the minimum integration time
      are set to 1 s and 0.5 s, which are also the smallest allowed values.
      Please note: Allowing for a too short step duration will result in spurious measurement 
                           data!
      Please note: This new option is only available for the CR mode, with the Fixed duration 
                           for each step option as well as the Integration time option selected 
                           (on the Acquisition page).

- Curve Discussion Element

- In the new Numerical box on the Layout page of the element editor the user 
      can now select whether the value of the standard deviation (Std. dev. or SD) and/or the 
      relative standard deviation (Rel. std. dev. or RSD) is to be displayed as part of the result of 
      the calculation of the mean value.

- On the Curve discussion page of the element editor the user can now select the 
      multiplication factor for the displayed value of the (relative) standard deviation.

- The calculated value of the (relative) standard deviation is displayed in the information box 
      of a data page.

- Interpolation Element
    - Under certain very special circumstances the Interpolation Element would crash.
      This has been solved.

- Graph / Table display
  - Entering/changing a value in a table
    - When entering a value in a table and hitting the Enter key, the new or modfied value is 
      now immediately displayed/updated in the corresponding graph. This is valid for both the 
      JobManager (that is during a job run) and the DataManager.

- RangeCalculator

- There was a problem showing the range for a Viscotester iQ measuring that was 
    automatically detected by the instrument and RheoWin. This has been solved.

2.49 Version 4.50.0010

(Released 27.10.2014)

Below is a list of things that are new and/or changed in version 4.50.0010 compared with 
version 4.50.00003 of RheoWin.

- Installation

- MARS I
    - The installation program now allows the installation of RheoWin for the new MARS I rheometer.
    - The new Temperature calibration tool, accessible from the JobManager Programs menu, is
      now part of the installation. A special installation key is needed to install this tool.

- DeviceManager

- All drivers
    - When running RheoWin in certain network configurations the message "Socket error while 
      receiving", which had nothing to do with RheoWin or the communication with any device, 
      could popup. This has been solved.

- Enabling/disabling LAN adapter for Connect Assist

- In order to prevent RheoWin from listening to LAN broadcast messages from the wrong rheometer,
      LAN adapters can now be enabled/disable in the Select Lan Adapter dialog. 
      This dialog is accessible by right clicking on the large rheometer button in the DeviceManager and 
      selecting the Select LAN adapter for Connect Assist command from the popup-menu.

- Driver for MARS 1

- There is a new driver for the new MARS I.

- The MARS firmware updater now also supports the MARS I.

- Drivers for Viscotester iQ
    - The inertia determination has been disabled for the Viscotester iQ. When an inertia value is
      needed it is read from the geometry tag using Connect Assist.
    - The Viscotester iQ firmware updater now also allows updating the Viscotester iQ user interface 
      (i.e. languages and graphics, etc.). See the Viscotester iQ instruction manual for more information

- The new  48 mm concentric cylinder temperature module (TM-LI-C48) and the matching 
      measuring geometries are now supported.

- Drivers for Viscotester 550
    - Under certain circumstances there was a problem with the gap value and the result M-factor for 
      parallel plate geometries. This has been solved.

- Drivers for communication with FTIR spectrometer
    - When running in simulation mode the driver will now also generate file names with time stamps.
  - Driver for Foculus FO323TC and FO323TB cameras

- There was a problem with saving the images as part of the RheoWin *.rwd file for the FO323TC 
      colour camera. This has been solved.
    - The camera selection options (any) and (smart selection), on the Additional data page of the
      Properties of ... dialog (in DeviceManager) of the rheometer with which the camera can be 
      used, currently do not work (this will be fixed in the next version of RheoWin).

- JobManager

- Information/Protocoll window
    - The version number of the firmware for the 2nd microcontroller in the Viscotester iQ is now 
      displayed also.

- Stopping a Job
    - On the General page of the Configuration - > Preferences dialog there is a new option 
      Confirm stop job. When this option is activated the operator will be shown a yes/no dialog 
      asking whether the job should be really stopped.

- Camera Element
    - Under certain circumstances loading and using saved camera setting did not work.
      This has been solved.

- Set Element
    - The checkboxes for resetting the normal force and for activating the nano-torque offset are
      now disabled/hidden for the Viscotester iQ.

- Temperature Set Element
    - The set normal force value was not displayed in the JobEditor and DataManager anymore.
      This has been solved.

- Rotation Ramp Element
    - Using the break criteria with a Viscostester iQ did not work properly. This has been solved.

- Rotation Stepped Ramp Element (Stationary Flow Curve Element)
    - The timing of the data acquisition for fixed duration steps, when acquiring FTIR spectra 
      simultaneously, has been corrected.

- All Oscillation Elements
    - The time-stamp (t_clock data channel) for FTIR spectra data has been corrected/optimized. 
      The time stamp of a FTIR spectra data file and its corresponding value in the the t_clock data 
      channel are now close to identical.

- Automatic temperature calibration tool
  - The  new  Temperature calibration tool, is now accessible from the JobManager Programs 
    menu. With this new tool the temperature calibration of any temperature modules can be 
    performed completely automatical. See the separate manual for a description of this tool.

2.50 Version 4.50.0011

(Released 03.11.2014)

Below is a list of things that are new and/or changed in version 4.50.0011 compared with 
version 4.50.0010 of RheoWin.

- DeviceManager

- Driver for Viscotester iQ
    - The driver is now compatible with the new gap setting routine, as introduced in firmware 
      version 1.03.000, for parallel plate and cone and plate geometries.

- The driver now supplies correct integration time values when the option Rotation > Acquisition 
      > Use automatic integration time was selected in the editor of the Rotation time element.

- Driver for Almemo devices (thermometer)
    - The driver for the Ahlborn ALMEMO 2590 universal measuring instrument (and compatible units)
      now also works when the Almemo device is connect to the computer using the special Almemo 
      USB cable and USB driver software.

2.51 Version 4.50.0012

(Released 13.11.2014)

Below is a list of things that are new and/or changed in version 4.50.0012 compared with 
version 4.50.0011 of RheoWin.

- General

- RheoWin version 4.50.0011 did not run under Windows XP, this has been solved.

- DeviceManager

- Geometries for Viscotester iQ
    - In RheoWin version 4.50.0011 there was a problem with Connect Assist, the 
      automatic geometry recognition, this has been solved.

- The name for the geometries CC27 DG/Ti and CC41 DG/Ti each contained a space character 
      too many, which causes problems with Connect Assist. 
      This has been solved.

- The cone and plate geometries geometries C35 2°/Ti, C60 2°/Ti, C35 3°/Ti, C60 3°/Ti,

C35 4°/Ti, C60 4°/Ti have been added.

- Viscotester iQ firmware updater

- When the Viscotester iQ firmware update can not be launched from the DeviceManagers 
      Properties of Viscotester iQ dialog, a message will now be displayed which tell the operator 
      to run the VTiQUpdate.exe from the c:\Program Files\Thermo\RheoWin\Drivers directory.

- MARS firmware updater

- In RheoWin version 4.50.0011 the MARS frimware updater did not work. This has been solved.

- Graph / Table display

- Axis scaling

- Thes scaling of the X-Axis has been improved.

2.52 Version 4.50.0013

(Released 19.12.2014)

Below is a list of things that are new and/or changed in version 4.50.0013 compared with 
version 4.50.0012 of RheoWin.

- DeviceManager

- Temperature signal for Viscotester iQ
    - When no TM-xx-x module or Pt100 sensor is connected to the Viscotester iQ the temperature 
      value in RheoWin would show an arbitrary (very high) value. This has been solved.

- MARS and camera (for RheoScope)
    - Various bugs with the image acquisition during oscillation measurements have been solved.

- For the image type JPG and PNG can now be selected.

- The automatic exposure time function has been made quicker.

- JobManager

- JobExplorer list

- When using the Save as ... command to save a Job in a directroy with a larger number of files 
      it could take a very long time to complete the action. This has been solved.

- When a folder icon is selected, there is a new command Edit all in the JobExplorer context 
      popup menu. Selecting this command will open a dialog in which the Rheometer and/or 
      Measuring geometry and/or Temperature controller for all Job files can be changes at the 
      same time. This should be used with care!

- All Oscillation Elements with a Viscotester iQ
    - In the oscillation elements the CS and CD mode were named FastCS and FastCD in 
      previous versions
      This has been changed into CS and CD.

- DataManager

- Saving images

- Camera images can now additionally be saved in JPG, PNG and GIF format.

2.53 Version 4.50.0017

(Released 19.02.2015)

Below is a list of things that are new and/or changed in version 4.50.0017 compared with 
version 4.50.0013 of RheoWin.

- DeviceManager

- Viscotester iQ 
    - The service/calibration date is now only checked for firmware versions 01.04.020 and higher

because it caused problems with earlier firmware versions.

- The temperature value displayed in the Device toolbar was not correct during oscillation
      measurements. This has been solved.

- Image acquisition

- Under certain circumstances there were problems with the image acquisition routines when 
      testing the camera before setting the camera properties in the DeviceManager. 
      This has been solved.

- JobManager

- Snapshot

- There was a problem when running a Snapshot test. This has been solved.

- Show data and wait Element
    - In the Show data and wait element the communication with a temperature control unit is
      now deactivated also when the communication with the device is deactivated.

- All OSC Elements

- Under certain circumstances the editors of these elements could crash. 
      This has been solved.

- Curvefit Element

- Under certain circumstances the parameter values displayed in the information window were
      not correct when the physical unit of the parameters were displayed together with the 
      parameters. This has been solved.

- In the Numerical group box on the Layout page of the element editor there are three new 
      entries Y value at X = with which the Y value of the curve-fit model can be calculated for 
      three X values. The result is displayed in the information window.
  - Crossover Element
    - The time t, the segment time t_seg and the temperature T are now available as QC criteria.

- DataManager

- Saving images

- Camera images can now additionally be saved as a video file in the WMV format by right
      clicking on the image area and selecting the Save as video command.

2.54 Version 4.60.0000

(Released 23.07.2015)

Below is a list of things that are new and/or changed in version 4.60.0000 compared with 
version 4.50.0017 of RheoWin.

- Installation

- MARS 40 and MARS 60

- The installation program now allows the installation of RheoWin for the new MARS 40 and

the new MARS 60 rheometer.

- Media files
    - A set of new Media files (images, small videos, application notes, short instructions, etc.) is 
      now part of the installation. These media files are used in the new Job example files and can
      of course be used in any other job as well.
    - Among the media files are videos and images which show how to apply the sample, how to 
      trim the sample, how to mount/dismount a measuring geometry etc.
    - The media files are installed in the following default directory (that is parallel to the Jobs, Data,
      Page, Template and Report directories):  C:\Users\Public\Documents\Thermo\RheoWin\Media.
  - Example and template files

- There is no possibility anymore to select which example and template files are to be installed.

All example Job, Data and Page files as well all templates files are now always installed

automatically.

- The set of example Job, Data and Page files has been completely renewed and extended.
    - The Job example files are installed in the Job\# Examples directory and lower level

sub-directories.

- The Data example files are installed in the Data\# Examples directory and lower level 
      sub-directories.

- The Page example files are installed in the Page\# Examples directory and lower level 
      sub-directories.

Please note: It is strongly recommended to have a close look at the new example files.

Please note: After modifying an example Job is should NOT be saved in the Job\# Examples 
                         directory or any lower level sub-directory of that directory, to prevent the modified 
                         Job from being deleted at the next update

- Spectra and MWD calculation tools    
    - Due to licence issues the Spectra and MWD calculation tools are NOT installed anymore
      when RheoWin is installed using the 098-5019 All instruments installatio key.

- In order to be able to install the new versions of the Spectra and MWD calculation tools
      new installation keys with new order numbers are needed. 
      The new Spectra calculation tool installation key order number is 098-5066.

The new MWD calculation tool  installation key order number is 098-5067.

- General

- The general look of both JobManager and DataManager has been modernized.

- DeviceManager

- MARS 40 and MARS 60 rheometers
    - There are two new drivers for the new MARS 40 and MARS 60.
    - The value of the air-pressure for the air-bearing is stored as part of the measured data.

- VTiQ and all MARS rheometers
    - There was a communication time-out problem when running multiple Jobs, with instruments 
      using TCP/IP communication, at the same time. This has been solved.

- Rheonaut module
    - The Rheonaut module can now be used with the TM-EL-H electrically heated hood for an
      improved sample temperature control.
      In order for this to work the following MARS firmware versions are needed:
           MARS 40 and MARS 60
               μP1 (Box microcontroller)    version 50.17.000

μP2 (Box DSP) 	        version 50.17.000 	
               μP3 (Stand microcontroller)  version 60.01.000
           MARS I and MARS III

μP1 (Box microcontroller)     version 50.17.000

μP2 (Box DSP) 	         version 50.17.000 	
               μP3 (Stand microcontroller)   version 50.21.000

- SC-AC-PC circulators
    - The temperature-offset table in the driver for these circulators can now be accessed by 
      the TempOffset calibration program.

- Almemo Multitemp
    - The driver of this auxilliarily device now retrieves and saves the device serial number.

- Connect Assist rotors (for MARS 40 and 60)  
    - The MSC calibration routine can (of course) also be used for Connect Assist rotors
      (when use with a MARS 40 or MARS 60). 
      The  resulting MSC (torque-mapping) values for these rotors are stored 
      in RheoWin (device.flp).

- MSC calibration
    - Under certain circumstances the MSC calibration did not work properly. This has been solved.

- JobManager

- Main menu toolbar icons

- The main toolbar icons have been modernized.

- Job Elements list

- All Job Element icons have been modernized.

- The General and Measurement Job Elements are now divided up into subgroups.

- Jobs and Templates file explorer
    - The file explorer icons have been modernized.

- Updating and adding example and template files
    - Thermo Fisher Scientific will supply updates for the example and template file on a regular basis.
      These updates will be distributed in the form of ZIP files that can be downloaded from the 
      RheoWin page on the www.rheowin.com website.

- The contents of such a ZIP file can be applied to an existing RheoWin installation using the new 
      Update example and template files dialog accessible from the Help > Internet/Update > Update > 
      Update example and template files menu.
    - By using the Replace command the operator can install a new version of the complete set of Job, 
      Data, and Page example files as well as all Media and Template files. By doing soing all current
      files in the Jobs\# Examples, Data\# Examples and Page\# Example directories and lower level

sub-directories will be deleted and replaced by new files and directories.
      Please note: This command will (of course) NOT delete file in other directories.

- By using the Add command the operator can add a single new example file or a few new 
      example files including media files to the current set of example files. 
      This command is meant to be used for supplying customers with specific examples on request.

- Job-Editor

- The icons in the Job-Editor dialog have been modernized.

- When the 21 CFR part 11 tools are installed, signature status information is now 
      displayed in the new Job-Editor status bar.

- Both the Application information area and the Devices area can be collapsed/expanded 
      regarding their height to have more space for the actual Job Element sequence.

- There is a new Application information area in the Job-Editor dialog with three button 
      and a text field:

- The text field is designated to display a short (one-line) text describing the Job
       - A click on the information i-button will show a window with is designated to display a 
         long (multi-line) text describing the Job in more detail. 
         The text description can be accompanied by an image or a video. 
         (For more information on this see below in the Message Element paragraph.)

- A click on the PDF document button will open a PDF file that is linked to the Job. 
         This functionality can be used to link a SOP document or an application note etc. directly 
         to the Job for quick and easy access.

- A click on the Edit button will open a dialog in which the short and the long text can
         be edited, and file names for an image, video and PDF file name can be selected.

- When no long text is defined, the information button is not displayed.

- When no document file name is specified, the PDF document button is not displayed.
       - In the new example Job files that are part of the installation many examples for the use of

the new Application information functionality can be found.

- Message Element
    - In the Message Element editor an image and video file can now be selected for display in 
      the Message window during a Job run.

- During Job run either the image or the video can be displayed, that is not both at the same time.

- The image or video will be scaled to a maximum width of 400 pixels and a maximum height 
      of 300 pixels.

- It is recommend to only use images or videos that already have the maximum width 
      and/or height.

- It is recommended to store the images and videos in the default Media directory, but any 
      other directory can be used as well.

- It is important to understand that the image and/or video is NOT stored in the Job file, only 
      the path to the image and/or video file is stored in the Job file.

- When the Message Element is only used to comment the Job Element sequence in the 
      Job-Editor, the text behind the element icon is displayed in a grey colour.
   - Lift Element
    - In the Message Element editor image and video files for each of the lift actions can 
      now be selected for display in the Message window during a Job run.
      (For more information on this see above in the Message Element paragraph.)

- The Lift Element dialog can be collapsed/expanded regarding its width. When the dialog is
      collapsed the message edit areas are not visible. 
    - Moving the lift to Standby position (after finding the zero point) is now an optional, integral part 
      of the Zero point lift action.

- For the MARS 40 and MARS 60 there is a new option Eject rotor (if possible) in the Lift apart 
      action. When this option is selected the rotor will automatically ejected from the drive motor 
      shaft before the instrument head (lift) moves upward.
      For all concentric cylinder geometries this always possible. For cone and plate and parellel plate
      geometries this is only possible when the sample is not too low viscous. For most special, non 
      standard, geometries this is not possible. 
      The rheometer firmware automatically decides whether ejecting the rotor is possible or not.

- OSC Temperature Ramp and OSC Temperature Step Elements

- In the editors of these elements there is a new page Extern on which the Trigger function 
      can be activated. 
      The Trigger functionality is the same as that in the OSC Time Curve Element.

- Curvefit Element

- Under certain circumstances there was a problem with the Herschel-Bulkley model. 
      This has been solved.

- DataManager

- Main menu toolbar icons

- The main toolbar icons have been modernized.

- Evaluation menu toolbar icons

- The evaluation toolbar icons have been modernized and enlarged.

- Data, Pages and Templates file explorer
    - The file explorer icons have been modernized.

- Saving images

- DataManager would crash when saving an image, that was stored in the Lurawave format, as a
      Bitmap file. This has been solved.

- Spectra calculation tool

- The Spectra calculation tool has been completely reprogrammed and now produces more 
      accurate results.

- MWD calculation tool

- The MWD calculation tool has been completely reprogrammed and now produces more 
      accurate results.
    Please note: The new MWD calculation tool needs a spectrum, calculated by the new
                         Spectra calculation tool, as input data. This means that the MWD calculation 
                         tool can not be used without the Spectra calculation tool.

- Graph / Table display

- Table

- The DataManager would crash when a file with a very long file name was loaded and the 
      mouse pointer was moved over the table header. This has been solved.

- When a table was exported to an Excel file the degree sign in the header of a data column 
      containing the phase angle. This has been solved.

- Graph

-  It was not posible change the filled/unfilled property of all curves of one data file at the same time. 
       This has been solved.

- RangeCalculator

- Some smaller bugs in the Range Calculator programm have been solved.

2.55 Version 4.60.0001

(Released 31.07.2015)

Below is a list of things that are new and/or changed in version 4.60.0001 compared with 
version 4.60.0000 of RheoWin.

- DeviceManager

- Connect Assist geometries for VTiQ, MARS 40 and MARS 60 rheometers
    - The Torque correction page in the Properties of a geometry dialog can now also be used in 
       the case of Connect Assist geometries.

- JobManager

- Job-Editor

- In the measurement element editors the range value limits (for the shear rate, shear stress, etc.)
      are immediately updated when a Connect Assist geometry was detected.

- DataManager

- MWD calculation tools    
    - On the Substance page of the MWD dialog the edit field and table column for GN0 have been 
      removed because the value for GN0 is calculated (and not needed as input).

2.56 Version 4.61.0000

(Released 27.11.2015)

Below is a list of things that are new and/or changed in version 4.61.0000 compared with 
version 4.60.0001 of RheoWin.

- Installation

- Installation of example and template files

- Some of the example job files contained wrong pathes to media files. This has been solved.
    - On some PC's the installation of the example and template files does not work and is quitted 
      with an error message and a dialog box. In case this happens close the dialog box by clicking 
      the Close button.
      The installation will then continue but the example and template files will not be installed.
      In this case the example files should be installed manually using the Help > Internet / Update > 
      Update > Update example and template files command. See the What's new information of
      version 4.60.0000 for more information on this.
      Please note: We are of course working on a solution for this problem.

- The zip file (RheoWin_Example_Files.zip ) which contains all example and template files is
      now installed in the Thermo > RheoWin folder in the Windows Public documents folder
  - ART service program
    - The ART service program is now always installed but can only be used without needing to 
      enter a password when the installation was performed using the General Key (098-5019).
      The ART service program is for use by qualified service engineers only!

- DeviceManager

- MARS 40 and MARS 60 
    - When runnning the inertia determination routine for the instrument alone (that is not for a 
      geometry) the new inertia value was not saved correctly. This has been solved.

- With the newest firmware the lift control buttons and the eject button on the control panel
      (on the front of the instrument itself) are now disabled during a measurement.
      These buttons were not enabled again at the end the of the inertia and MSC determination
      routines. This has been solved. 
    - An erroneous update message would appear when a Connect Assist Adapter was
      attached to the instruments drive motor shaft. 
      This has been solved, the message is not displayed anymore.
  - MTMC and UTMC
    - The maximum number of temperature offset values in a temperature offset table is now 
      limited to 9 since the firmware can not handle more.
  - FTIR spectrometer
    - In the drivers.ini file, the temporary directory in which the FTIR spectra data is saved can 
      now be modified by adding an entry like:
          [IRSPECTRO]
          SpectraTempPath=C:\SpectraTemp\
      Please note: The above path is just an example.
                           The last character of the path string must be a "\"

- In the drivers.ini file, the use of DDE commands for use with the Omnic software can
      activated by adding the following entry:

[IRSPECTRO]
          Raman=1
      This is used for the commands CollectSample and CollectBackground.

- SER tool with Connect Assist
    - The SER tool with Connect Assist was not correctly handled and not entered in the list of
      geometries after it was recognized by the instrument. This has been solved.

- Jobrun.exe

- Launch Job from Windows destop or Windows explorer
    - When running a Job from the Windows desktop or from the Windows explorer an error 
      message would appear at the very end of the Job. This has been solved.

- JobManager
  - RheoWizard
    - The RheoWizard would produce a non-functional Job when selecting Chocolate from 
      he List of subtances.This has been solved.

- Lift control icons
    - The Lift control icons in the Device toolbar and in the Manual control window are now 
      different fo rheometers in which the table moves up/down compared with those rheometer
      where the measuring head moves up/down.

- New Fill Assist element

- There is a new Fill Assist element which allows the use of the Fill Assist tool in a RheoWin
      job in combination with the Viscotester iQ. For more information on the Fill Assist tool see 
      the HAAKE Viscotester iQ reference manual version 1.6 or higher.

2.57 Version 4.61.0003

(Released 04.02.2016)

Below is a list of things that are new and/or changed in version 4.61.0003 compared with 
version 4.61.0000 of RheoWin.

- DeviceManager

- MARS I, MARS III, MARS 40 and MARS 60 
    - The lowest allowed value for the oscillation frequency is now 10^-6 Hz.

- Viscotester iQ
    - The Diagnosis Save function will now write more information in the diagnosis file.
  - FTIR spectrometer
    - Some smaller bugs were removed.

- JobManager
  - Jobrun
    - Under certain circumstances the Goto-Element would crash when the (Data) Autosave 
      function was called. This has been solved.

2.58 Version 4.62.0000

(Released 12.04.2016)

Below is a list of things that are new and/or changed in version 4.62.0000 compared with 
version 4.61.0003 of RheoWin.

- Installation

- Viscotester iQ Air

- The installation program now allows the installation of RheoWin for the new 
      Viscotester iQ Air rheometer.

- DeviceManager

- Viscotester iQ Air rheometer
    - There is a new driver VTiQAir.dll for the new Viscotester iQ Air.
      For the optional TM-xx-x temperature control modules the VTiQ Air uses the same 
      driver as the 'normal' VTiQ, i.e. the VTiQT.dll driver.

- MARS I, III, 40 and 60
    - The inertia determination routine now uses CD Oscillation mode at two different (large) 
      amplitudes to measure the moment of inertia.

- The available options in the Options box on the Options page of the Properties of 
      'MARS xx' editor are now sorted/ordered differently.

- There are two new options for the Oscillation mode in the Options box on the Options 
      page of the Properties of 'MARS xx' editor:
          - Active compliance correction CD-OSC

- Active inertia correction CS-OSC
      These new options are activated by default. 
      Please note: When these corrections are activated the measurement results may
                           (slightly) differ from those previously measured without these corrections. 
                           For situations where that is not desired these corrections can be deactivated.
      Please note: When the new firmware is not installed or the options are deactivated, the 
                           firmware will use the passive compliance correction and passive inertia 
                           correction which were standard until now.

Please note: New MARS firmware versions are needed for these options to work.
                           The mP1 microcontroller firmware version must be 50.19.001 or higher.

The mP2 DSP firmware version must be 50.17.165 or higher.
                            (check the www.rheowin.com/firmware.htm web-page for the availibility of 
                             such firmware versions)
  - Measuring Geometries

- The handling of the Solid clamp geometry was not correct for both the version with 
      the classical conical coupling and the new Connect Assist version. 
      This has been solved.

- Viscotester D and E drivers

- The Temperature offset tables were not used correctly. This has been solved.

- JobManager

- JobEditor
    - The software handling of Connect Assist geometries (MARS 40, MARS 60 and VTiQ) has 
      been modified. Instead of displaying one or more message windows a green or red status
      light is now displayed between the geometry name and the Connect Assist button in the 
      JobEditor dialog.
    - The Connect Assist functionality (MARS 40, MARS 60 and VTiQ) can now be completely 
      disabled by selecting the option Use geometry defined in Job (disable Connect Assist) in 
      the Connect Assist settings dialog. 
      Please note: The Connect Assist settings dialog is accessed by right clicking on the
                           Measuring geometry drop-down list or on the Connect Assist button.

- Rotation Ramp elements
    - Under certain circumstances the Take from previous options for the shear rate or shear 
      stress set value did not work properly. This has been solved.

2.59 Version 4.62.0003

(Released 10.05.2016)

Below is a list of things that are new and/or changed in version 4.62.0003 compared with 
version 4.62.0000 of RheoWin.

- DeviceManager

- Viscotester iQ (Air) rheometer
    - The diagnosis window for these instruments has been modified.

- The automatic integration time (ROT Elements) functionality has been improved.

Please note: For this to work with the VTiQ, firmware version V1 must 1.10.000 or higher.

For the VTiQ this is implemented from the start.

- UTC drivers

- Since the UTC control box only works with a baudrate of 4800, the baudrates 9600 and 
      19200 have been removed from the baudrate selection box.

- JobManager

- Device Toolbar
    - The device toolbar is now automatically disabled when the automatic temperature
      calibration tool is running.

- JobEditor
    - The software handling of Connect Assist geometries (MARS 40, MARS 60 and VTiQ) has 
      been further improved.

- Under certain circumstances an error message Hades Error 36 would popup at the start 
      of a Job. This has been solved.

- Axial Time element
    - The axial strain value was not calculated correctly. This has been solved.
    - The gap change values Dh and D%h are now measured and stored, just as in the 
      Axial Ramp element.

2.60 Version 4.63.0000

(Released 20.07.2016)

Below is a list of things that are new and/or changed in version 4.63.0000 compared with 
version 4.62.0003 of RheoWin.

- DeviceManager

- MARS 40 and 60 drivers
    - The actual lift speed did not correspond to the lift speed values selected in the Lift Element. 
      This has been solved, the actual lift speed now corresponds to the selected value.
      Because the existing selectable lift speed values were relatively low, four new lift speed values
      (5, 10, 20 and 50 mm/s) have been added.

Please note: New MARS firmware versions are needed for these options to work.
                           The mP1 microcontroller firmware version must be 50.21.000 or higher.

The mP2 DSP firmware version must be 50.19.000 or higher.
                           The mP3 firmware version must be 61.02.000 or higher.
                            (check the www.rheowin.com/firmware.htm web-page for the availibility of 
                             such firmware versions)

- JobManager

- Lift Element
    - The lift speed control has been modified. The operator can now define a gap value above which 
      the lift will move at it's maximum speed (this is a device dependend value) and below which the 
      lift will either move with the selected speed value (Use Speed option) or the lift will apply a set 
      normal force (Use Autotension option) to the sample.
    - The gap at which the lift speed is changed is defined by the new When gap <= xxx.x mm value 
      in the Lift Element editor.

Please note: The above is valid for all (!) Rheometer models.
  - Rot Temperature Ramp Element
    - Data measured by a Job running internally in a VTiQ (Air) was not displayed correctly.
      This has been solved.

- Rot Ramp Element
    - Under (rare) circumstances the Rot Ramp element would hang or crash at the beginning or the 
      end of the ramp. This has been solved.

- Axial Time Element
    - Under very special circumstances the element editor would crash because of a division by zero.
      This has been solved.

- Yield-Stress Evaluation Element
    - Under (very rare) circumstances the Yield-Stress value calculated during a Job run could be 
      different (i.e. not correct) from the value calculated in DataManager. This has been solved.

- Temperature Calibration Tool

- The (optional) temperature calibration tool program has been updated. 
    Some smaller bugs have been fixed.

2.61 Version 4.63.0001

(Released 22.07.2016)

Below is a list of things that are new and/or changed in version 4.63.0001 compared with 
version 4.63.0000 of RheoWin.

- JobManager

- Curve discussion element

- The QC-result was not displayed correctly for the Mean value calculation. This has been solved.

2.62 Version 4.63.0002

(Released 18.08.2016)

Below is a list of things that are new and/or changed in version 4.63.0002 compared with 
version 4.63.0001 of RheoWin.

- DeviceManager

- Imaging DLL for Camera/RheoScope
    - In version 4.63.000x the camera did not work because the Imaging.dll that was automatically 
      installed does not work with (the older) FGControl version 2.3.3.1 which was used until know.

      Starting from this version RheoWin (i.e. the Imaging.dll) works with FGControl version 2.6.0.2 
      by default. This new FGControl version is available on the RheoWin CD and can also be 
      downloaded from www.rheowin.com/rheowin46.htm. See the HAAKE RheoWin User Guide 
      Camera installation version 2.3 on how to install the FGControl software.

      Users who do not want to use the new FGControl version 2.6.0.2, can manually install a version 
      of the Imaging.dll which is compatible with FGControl 2.3.3.1. This imaging.dll (see the
      Imaging.dll for FGControl 2.3.3.1 directory in the zip file) is part of the rhw4630002_complete.zip 
      file which can be downloaded from the RheoWin web-site. This file is also available on the 
      RheoWin CD in RheoWin\Imaging.dll for FGControl 2.3.3.1 directory.

2.63 Version 4.63.0003

(Released 09.11.2016)

Below is a list of things that are new and/or changed in version 4.63.0003 compared with 
version 4.63.0002 of RheoWin.

- DeviceManager

- MARS I and MARS III drivers
    - The actual lift speed did not correspond to the lift speed values selected in the Lift Element.
      This has been solved, the actual lift speed now corresponds to the selected value.
      Because the existing selectable lift speed values were relatively low, four new lift speed
      values (5, 10, 20 and 50 mm/s) have been added.

Please note: New MARS I / MARS III firmware versions are needed for this to work.
                           The mP1 Box microcontroller firmware version must be 50.23.000 or higher.

The mP2 Box DSP firmware version must be 50.18.000 or higher.
                           The mP3 Stand firmware version must be 50.25.000 or higher.
                           (check the www.rheowin.com/firmware.htm web-page for the availibility of 
                            such firmware versions)

- JobManager

- Axial Ramp Element (MARS I, III, 40, 60)
    - The communication between the Axial-Ramp Element in RheoWin and the Axial-Ramp control 
      in the firmware has been modified in order to optimize the Axial Ramp performance.
      Please note: New MARS I / MARS III firmware versions are needed for this to work.
                           The mP1 Box microcontroller firmware version must be 50.23.000 or higher.

The mP2 Box DSP firmware version must be 50.18.000 or higher.
                           The mP3 Stand firmware version must be 50.25.000 or higher.
                           (check the www.rheowin.com/firmware.htm web-page for the availibility of 
                            such firmware versions)

Please note: New MARS 40 / MARS 60 firmware versions are needed for this to work.
                           The mP1 Box microcontroller firmware version must be 50.23.000 or higher.

The mP2 Box DSP firmware version must be 50.19.000 or higher.
                           The mP3 Stand firmware version must be 61.03.000 or higher.
                           (check the www.rheowin.com/firmware.htm web-page for the availibility of 
                            such firmware versions).

2.63 Version 4.63.0004

(Released 24.01.2017)

Below is a list of things that are new and/or changed in version 4.63.0004 compared with 
version 4.63.0003 of RheoWin.

- DeviceManager

- Imaging DLL (RheoScope Module)
    -.The scale gauge that is displayed on top of an image acquired with the RheoScope module
      was slightly wrong. This has been corrected.

Please note: This correction only applies to images acquired with RheoWin 4.63.0004 or 
                          newer, that is NOT to images acquired as part of measurements made with 
                          earlier RheoWin versions.

Please note: Due to the limited screen resolution of computer monitors the accuracy of the scale 
                          gauge is limited to values in the range of 1 µm.

----------

3 Limitations and known issues

- RheoWin 4.63.00xx can not be installed and consequently will NOT run and/or is 
  NOT supported for use under the following Windows operating systems:
  - Windows 3.x or even older versions of Windows
  - Windows 95

- Windows 98 with Y2K update and Internet Explorer 4.01 SP2

- Windows 98 SE

- Windows ME
  - Windows NT 3.x

- Windows NT4.0 with Service Pack 6 and Internet Explorer 6

- Windows 2000 with Service Pack 1

- RheoWin 4.63.00xx is currently not supported for use under the following
  operating systems :

- Windows Vista with or without any Service Pack.

- The new FGControl driver for the (RheoScope) Foculus camera is compatible with
  the 32-bit and 64-bit Windows versions of Windows 7, Windows 8 and Windows 8.1.

- The older FOControl driver for the Foculus camera is compatible with 
  Windows XP 32-bit only.

- The driver for the previously used Sony XCD-X710 camera is compatible with 
  Windows XP 32-bit only.
  A small separate RheoWin update is needed to make the driver work.

- Administrator privileges are needed to be able to install RheoWin 4.63.00xx.

- Some languages (in the language file) apart from German and English are 
  not 100% complete.

An updated language file will be made available on the RheoWin web-site.

- When a Job is running in RheoWin JobManager the Windows TaskManager might show a 
  high percentage of CPU usage by the JobManager. This only means that JobManager has
  been given that percentage by the Windows Operating System because no other program 
  needs a lot that CPU power.

----------

4 Contact Thermo Fisher Scientific

If you have any questions and or suggestion regarding HAAKE RheoWin

please send an e-mail to:

support.mc.de@thermofisher.com

----------

This file was last updated on: 24.01.2017 by Jint Nijman